## Slide 1: CCDs in Astronomy
History of CCDs
How do CCDs work ?
Advantages of CCDs
Calibrations
Observations with a CCD
Charge Coupled Device
www.sliderbase.com
Notes: CCDs in Astronomy
History of CCDs
How do CCDs work ?
Advantages of CCDs
Calibrations
Observations with a CCD
Charge Coupled Device
CCDs in Astronomy
History of CCDs
How do CCDs work ?
Advantages of CCDs
Calibrations
Observations with a CCD
Charge Coupled Device

## Slide 2: Photographic Imaging
Photographic Plates: 100m thick emulsion spread over a glass base
    Solidified gelatin w/silver halide salt grains
“Pixel size” (grain size): 6 m
How it works: multiple photons strike silver halide grains – give off electrons and form silver atoms within grains
Developing converts exposed grains into opaque silver
www.sliderbase.com
Notes: Photographic Imaging
Photographic Plates: 100mm thick emulsion spread over a glass base
Solidified gelatin w/silver halide salt grains
“Pixel size” (grain size): 6 mm
How it works: multiple photons strike silver halide grains – give off electrons and form silver atoms within grains
Developing converts exposed grains into opaque silver
Photographic Imaging
Photographic Plates: 100mm thick emulsion spread over a glass base
Solidified gelatin w/silver halide salt grains
“Pixel size” (grain size): 6 mm
How it works: multiple photons strike silver halide grains – give off electrons and form silver atoms within grains
Developing converts exposed grains into opaque silver

## Slide 3: Photomultiplier Tubes
“Single pixel” detector made of alkali metals
Photon strikes detector and knocks off one electron
That electron creates a cascade effect that ends in many electrons at the end of the detector
    The incoming photon must have enough energy to knock loose the first electron or it is not “seen”
www.sliderbase.com
Notes: Photomultiplier Tubes
“Single pixel” detector made of alkali metals
Photon strikes detector and knocks off one electron
That electron creates a cascade effect that ends in many electrons at the end of the detector
The incoming photon must have enough energy to knock loose the first electron or it is not “seen”
Photomultiplier Tubes
“Single pixel” detector made of alkali metals
Photon strikes detector and knocks off one electron
That electron creates a cascade effect that ends in many electrons at the end of the detector
The incoming photon must have enough energy to knock loose the first electron or it is not “seen”

## Slide 4: CCD History
First developed in the 1960s as memory storage devices
  Sensitivity to light suggested imaging possibilities
In the 1970s, CCDs were used primarily as experimental devices
In the 1980s, their use became more widespread
By the 1990s they’d essentially completely taken over almost all imaging applications
  video and still cameras, scanners etc.
Astronomy is a highly demanding application
  low light
  noise
  cosmetics
CCD image of Uranus from 1975 (JPL & UofA)
8900 Å
61”, Mt. Bigelow
Methane at the south pole
www.sliderbase.com
Notes: CCD History
First developed in the 1960s as memory storage devices
Sensitivity to light suggested imaging possibilities
In the 1970s, CCDs were used primarily as experimental devices
In the 1980s, their use became more widespread
By the 1990s they’d essentially completely taken over almost all imaging applications
video and still cameras, scanners etc.
Astronomy is a highly demanding application
low light
noise
cosmetics
CCD image of Uranus from 1975 (JPL & UofA)
8900 Å
61”, Mt. Bigelow
Methane at the south pole
CCD History
First developed in the 1960s as memory storage devices
Sensitivity to light suggested imaging possibilities
In the 1970s, CCDs were used primarily as experimental devices
In the 1980s, their use became more widespread
By the 1990s they’d essentially completely taken over almost all imaging applications
video and still cameras, scanners etc.
Astronomy is a highly demanding application
low light
noise
cosmetics
CCD image of Uranus from 1975 (JPL & UofA)
8900 Å
61”, Mt. Bigelow
Methane at the south pole

## Slide 5: How Does a CCD Work?
Rain = Photons
Water = Charge (photon strikes silicon semiconductor surface and knocks an electron loose by the photoelectric effect)
Buckets = pixels (electrons accumulate in “potential wells;” depth represents how much charge each pixel can hold)
The charge in each line of pixels is shifted to the readout register
The charge in each pixel is counted
www.sliderbase.com
Notes: How Does a CCD Work?
Rain = Photons
Water = Charge (photon strikes silicon semiconductor surface and knocks an electron loose by the photoelectric effect)
Buckets = pixels (electrons accumulate in “potential wells;” depth represents how much charge each pixel can hold)
The charge in each line of pixels is shifted to the readout register
The charge in each pixel is counted
How Does a CCD Work?
Rain = Photons
Water = Charge (photon strikes silicon semiconductor surface and knocks an electron loose by the photoelectric effect)
Buckets = pixels (electrons accumulate in “potential wells;” depth represents how much charge each pixel can hold)
The charge in each line of pixels is shifted to the readout register
The charge in each pixel is counted

## Slide 6: How CCDs Work
9 pixel CCD, an output register, and an amplifier
Pixels divided into 3 regions to create potential wells
  during an exposure, the higher potential of the central region (yellow) collects electrons
  during readout, the potentials are changed to transfer charges to the next region.
Electrodes
To Output amplification
Electrons
(a)
Output
register
Pixel
(b)
www.sliderbase.com
Notes: How CCDs Work
9 pixel CCD, an output register, and an amplifier
Pixels divided into 3 regions to create potential wells
during an exposure, the higher potential of the central region (yellow) collects electrons
during readout, the potentials are changed to transfer charges to the next region.
How CCDs Work
9 pixel CCD, an output register, and an amplifier
Pixels divided into 3 regions to create potential wells
during an exposure, the higher potential of the central region (yellow) collects electrons
during readout, the potentials are changed to transfer charges to the next region.

## Slide 7
Electrons transfered from pixel to pixel
Charges guided to the output register
Horizontal charge transfer is paused while charge packages at the output register are transfered vertically to an output amplifier and then read one by one
The cycle repeats until all the charges are read
Readout times can be as long as a few minutes
(b)
(a)
Impurity (doping)
www.sliderbase.com
Notes: Electrons transfered from pixel to pixel
Charges guided to the output register
Horizontal charge transfer is paused while charge packages at the output register are transfered vertically to an output amplifier and then read one by one
The cycle repeats until all the charges are read
Readout times can be as long as a few minutes
Electrons transfered from pixel to pixel
Charges guided to the output register
Horizontal charge transfer is paused while charge packages at the output register are transfered vertically to an output amplifier and then read one by one
The cycle repeats until all the charges are read
Readout times can be as long as a few minutes

## Slide 8: What moves the charge?
Charge transfer in a CCD
Changing the voltages φ1 and φ2 moves the location of the potential well to the right, and the electrons follow along
www.sliderbase.com
Notes: What moves the charge?
Charge transfer in a CCD
Changing the voltages φ1 and φ2 moves the location of the potential well to the right, and the electrons follow along
What moves the charge?
Charge transfer in a CCD
Changing the voltages φ1 and φ2 moves the location of the potential well to the right, and the electrons follow along

## Slide 9: CCD Advantages
Wide dynamic range (can measure both very faint targets and very bright ones)
Low noise
High QE
Accuracy (both linearity and stability)
Sensitivity over a wide spectral region (to 1m)
Dimensionally stable
Regular grid of pixels
Digital
CCD mosaic from Kitt Peak
Four 2048x2048 pixels
www.sliderbase.com
Notes: CCD Advantages
Wide dynamic range (can measure both very faint targets and very bright ones)
Low noise
High QE
Accuracy (both linearity and stability)
Sensitivity over a wide spectral region (to 1 mm)
Dimensionally stable
Regular grid of pixels
Digital
CCD mosaic from Kitt Peak
Four 2048x2048 pixels
CCD Advantages
Wide dynamic range (can measure both very faint targets and very bright ones)
Low noise
High QE
Accuracy (both linearity and stability)
Sensitivity over a wide spectral region (to 1 mm)
Dimensionally stable
Regular grid of pixels
Digital
CCD mosaic from Kitt Peak
Four 2048x2048 pixels

## Slide 10: Quantum Efficiency
QE is a measure of how efficient a device is in turning input energy (in this case light) into a measurable signal.
Greater efficiency means that more data can be gathered in a shorter time, or that in the same time you can measure a fainter signal.
Best film
Amateur CCD
Professional CCD
www.sliderbase.com
Notes: QE is a measure of how efficient a device is in turning input energy (in this case light) into a measurable signal.
Quantum Efficiency
Greater efficiency means that more data can be gathered in a shorter time, or that in the same time you can measure a fainter signal.
QE is a measure of how efficient a device is in turning input energy (in this case light) into a measurable signal.
Quantum Efficiency
Greater efficiency means that more data can be gathered in a shorter time, or that in the same time you can measure a fainter signal.

## Slide 11: Comparing Detector QEs
www.sliderbase.com
Notes: Comparing Detector QEs
Comparing Detector QEs

## Slide 12: Linearity
CCDs have a linear response to light, i.e. the measured signal is directly proportional to the amount of light which was received. This is not true for film.
A linear response means that if the exposure is doubled, then the measurable signal will double. Also, twice the signal means the source is twice as bright.
CCD linear response
Film non-linear response
www.sliderbase.com
Notes: Linearity
CCDs have a linear response to light, i.e. the measured signal is directly proportional to the amount of light which was received. This is not true for film.
A linear response means that if the exposure is doubled, then the measurable signal will double. Also, twice the signal means the source is twice as bright.
CCD linear response
Film non-linear response
Linearity
CCDs have a linear response to light, i.e. the measured signal is directly proportional to the amount of light which was received. This is not true for film.
A linear response means that if the exposure is doubled, then the measurable signal will double. Also, twice the signal means the source is twice as bright.
CCD linear response
Film non-linear response

## Slide 13: Designing a CCD
Most commercial CCDs are “front-side illuminated”
  A 3-d circuit on a base of silicon (the light sensitive layer)
  Light has to go through the circuitry, which causes losses
Astronomical CCDs are “back-side illuminated” with QEs of 90% or greater
  silicon is be thinned to a few tens of microns
  need to support the silicon.
  some charge diffusion in the silicon
Anti-reflection coating applied to the CCD surface reduces loses
Front-side illuminated CCDs have low blue QE
  devices can be coated with “Lumigen” – an organic substance similar to the “glow” in highlighter markers (Lumigen converts blue/UV photons to 520 nm, where the CCD has higher QE)
www.sliderbase.com
Notes: Designing a CCD
Most commercial CCDs are “front-side illuminated”
A 3-d circuit on a base of silicon (the light sensitive layer)
Light has to go through the circuitry, which causes losses
Astronomical CCDs are “back-side illuminated” with QEs of 90% or greater
silicon is be thinned to a few tens of microns
need to support the silicon.
some charge diffusion in the silicon
Anti-reflection coating applied to the CCD surface reduces loses
Front-side illuminated CCDs have low blue QE
devices can be coated with “Lumigen” – an organic substance similar to the “glow” in highlighter markers (Lumigen converts blue/UV photons to 520 nm, where the CCD has higher QE)
Designing a CCD
Most commercial CCDs are “front-side illuminated”
A 3-d circuit on a base of silicon (the light sensitive layer)
Light has to go through the circuitry, which causes losses
Astronomical CCDs are “back-side illuminated” with QEs of 90% or greater
silicon is be thinned to a few tens of microns
need to support the silicon.
some charge diffusion in the silicon
Anti-reflection coating applied to the CCD surface reduces loses
Front-side illuminated CCDs have low blue QE
devices can be coated with “Lumigen” – an organic substance similar to the “glow” in highlighter markers (Lumigen converts blue/UV photons to 520 nm, where the CCD has higher QE)

## Slide 14: Readout Noise -
A CCD has an analog output
  Photons are converted to a charge and then to a voltage for measurement.
  An amplifier on the CCD boosts the signal to a useful level
Is it possible to measure exactly how many photons fell on each pixel?
  No. The noise inherent in the conversion and amplification process introduces some noise
  The lowest noise CCDs now used in astronomy have a readout noise (RMS error ~2e–)
How accurately can we measure the number of photons detected by a CCD pixel?
www.sliderbase.com
Notes: Readout Noise -
A CCD has an analog output
Photons are converted to a charge and then to a voltage for measurement.
An amplifier on the CCD boosts the signal to a useful level
Is it possible to measure exactly how many photons fell on each pixel?
No. The noise inherent in the conversion and amplification process introduces some noise
The lowest noise CCDs now used in astronomy have a readout noise (RMS error ~2e–)
How accurately can we measure the number of photons detected by a CCD pixel?
Readout Noise -
A CCD has an analog output
Photons are converted to a charge and then to a voltage for measurement.
An amplifier on the CCD boosts the signal to a useful level
Is it possible to measure exactly how many photons fell on each pixel?
No. The noise inherent in the conversion and amplification process introduces some noise
The lowest noise CCDs now used in astronomy have a readout noise (RMS error ~2e–)
How accurately can we measure the number of photons detected by a CCD pixel?

## Slide 15: Bias
The CCD amplifier also introduces a “bias level” to the output voltage
  typically a few hundred electrons
The bias level is measured from the “overscan” region and subtracted off
“Bias structure” may also be present in a 2D image
The electronics as well as the physical make-up of a CCD can also imprint a faint background structure on the images.
low-level
structure in
the bias
www.sliderbase.com
Notes: Bias
The CCD amplifier also introduces a “bias level” to the output voltage
typically a few hundred electrons
The bias level is measured from the “overscan” region and subtracted off
“Bias structure” may also be present in a 2D image
The electronics as well as the physical make-up of a CCD can also imprint a faint background structure on the images.
low-level
structure in
the bias
Bias
The CCD amplifier also introduces a “bias level” to the output voltage
typically a few hundred electrons
The bias level is measured from the “overscan” region and subtracted off
“Bias structure” may also be present in a 2D image
The electronics as well as the physical make-up of a CCD can also imprint a faint background structure on the images.
low-level
structure in
the bias

## Slide 16: Charge Transfer Efficiency (CTE)
How efficiently can charge be moved across the pixels and the readout register? Will every electron be moved or will some be lost?
The earliest CCDs had a CTE of only ~98%
Today CTE is typically better than 99·995% in commercial devices (“4 nines”)
Much higher in scientific devices - 99·9999% (5-6 “nines”).
Poor CTE means that not all of the photons which arrived on the CCD will be counted, and the further from the readout register the worse the effect.
www.sliderbase.com
Notes: How efficiently can charge be moved across the pixels and the readout register? Will every electron be moved or will some be lost?
Charge Transfer Efficiency (CTE)
The earliest CCDs had a CTE of only ~98%
Today CTE is typically better than 99·995% in commercial devices (“4 nines”)
Much higher in scientific devices - 99·9999% (5-6 “nines”).
Poor CTE means that not all of the photons which arrived on the CCD will be counted, and the further from the readout register the worse the effect.
How efficiently can charge be moved across the pixels and the readout register? Will every electron be moved or will some be lost?
Charge Transfer Efficiency (CTE)
The earliest CCDs had a CTE of only ~98%
Today CTE is typically better than 99·995% in commercial devices (“4 nines”)
Much higher in scientific devices - 99·9999% (5-6 “nines”).
Poor CTE means that not all of the photons which arrived on the CCD will be counted, and the further from the readout register the worse the effect.

## Slide 17: Saturation
What if a pixel’s potential well “fills up” with electrons? The physical size of the pixel determines how much charge it can hold. Larger pixels can hold more charge.
Pixels are saturated when their potential wells are full. Electrons “bleed” along columns into nearby pixels
As a CCD pixel nears saturation, the response of the pixel becomes non-linear
The data number read out from a saturated pixel cannot exceed the largest number allowed by the “analog to digital converter” that converts the voltage to a digital signal (typically 16 bit, or 65,536)
Bleeding from bright stars
www.sliderbase.com
Notes: What if a pixel’s potential well “fills up” with electrons? The physical size of the pixel determines how much charge it can hold. Larger pixels can hold more charge.
Saturation
Pixels are saturated when their potential wells are full. Electrons “bleed” along columns into nearby pixels
As a CCD pixel nears saturation, the response of the pixel becomes non-linear
The data number read out from a saturated pixel cannot exceed the largest number allowed by the “analog to digital converter” that converts the voltage to a digital signal (typically 16 bit, or 65,536)
Bleeding from bright stars
What if a pixel’s potential well “fills up” with electrons? The physical size of the pixel determines how much charge it can hold. Larger pixels can hold more charge.
Saturation
Pixels are saturated when their potential wells are full. Electrons “bleed” along columns into nearby pixels
As a CCD pixel nears saturation, the response of the pixel becomes non-linear
The data number read out from a saturated pixel cannot exceed the largest number allowed by the “analog to digital converter” that converts the voltage to a digital signal (typically 16 bit, or 65,536)
Bleeding from bright stars

## Slide 18: Thermal Noise or Dark Current
The finite temperature of the CCD leads to the production of thermally induced electrons in the silicon
  Dark current increases linearly with time
A function of the temperature of the CCD
  CCDs cooled to around 170°K (-100°C) to reduce thermal noise
Dark current can be removed with careful calibration
www.sliderbase.com
Notes: Thermal Noise or Dark Current
The finite temperature of the CCD leads to the production of thermally induced electrons in the silicon
Dark current increases linearly with time
A function of the temperature of the CCD
CCDs cooled to around 170°K (-100°C) to reduce thermal noise
Dark current can be removed with careful calibration
Thermal Noise or Dark Current
The finite temperature of the CCD leads to the production of thermally induced electrons in the silicon
Dark current increases linearly with time
A function of the temperature of the CCD
CCDs cooled to around 170°K (-100°C) to reduce thermal noise
Dark current can be removed with careful calibration

## Slide 19: A few more problems with CCDs:
The amplifier in some CCDs glows!
Defects in the silicon wafer can cause cosmetic problems
CCDs are sensitive to cosmic rays
Bad columns
Cosmic rays
Glowing amplifier
www.sliderbase.com
Notes: A few more problems with CCDs:
The amplifier in some CCDs glows!
Defects in the silicon wafer can cause cosmetic problems
CCDs are sensitive to cosmic rays
Bad columns
Cosmic rays
Glowing amplifier
A few more problems with CCDs:
The amplifier in some CCDs glows!
Defects in the silicon wafer can cause cosmetic problems
CCDs are sensitive to cosmic rays
Bad columns
Cosmic rays
Glowing amplifier

## Slide 20: CCD Characterization
CCDs are characterized before they are put on a telescope.
The parameters which are needed are:
The amplifier gain – how many electrons per count.
The linearity of the amplifier and electronics – there will always be some slight variation from perfection.
QE and CTE – how good is the CCD.
Any cosmetic or electronic blemishes (“trapping sites”, etc.) – every CCD is unique!
www.sliderbase.com
Notes: CCDs are characterized before they are put on a telescope.
CCD Characterization
The parameters which are needed are:
The amplifier gain – how many electrons per count.
The linearity of the amplifier and electronics – there will always be some slight variation from perfection.
QE and CTE – how good is the CCD.
Any cosmetic or electronic blemishes (“trapping sites”, etc.) – every CCD is unique!
CCDs are characterized before they are put on a telescope.
CCD Characterization
The parameters which are needed are:
The amplifier gain – how many electrons per count.
The linearity of the amplifier and electronics – there will always be some slight variation from perfection.
QE and CTE – how good is the CCD.
Any cosmetic or electronic blemishes (“trapping sites”, etc.) – every CCD is unique!

## Slide 21: Gain and Readout Noise
Noise (ADU) as a function of the signal (ADU)
www.sliderbase.com
Notes: Gain and Readout Noise
Noise (ADU) as a function of the signal (ADU)
Gain and Readout Noise
Noise (ADU) as a function of the signal (ADU)

## Slide 22: Observing with a CCD
1, 10, 100 and 1000 sec exposures of M100
S/N ratio improves with exposure time
Readout noise dominates in the shortest exposure
Photon noise in the sky dominates for the longest exposure
www.sliderbase.com
Notes: Observing with a CCD
1, 10, 100 and 1000 sec exposures of M100
S/N ratio improves with exposure time
Readout noise dominates in the shortest exposure
Photon noise in the sky dominates for the longest exposure
Observing with a CCD
1, 10, 100 and 1000 sec exposures of M100
S/N ratio improves with exposure time
Readout noise dominates in the shortest exposure
Photon noise in the sky dominates for the longest exposure

## Slide 23: CCD Calibrations
NGC 2736, part of the Vela SN remnant.
Basic calibrations include BIAS, DARK and FLAT FIELD
www.sliderbase.com
Notes: CCD Calibrations
NGC 2736, part of the Vela SN remnant.
Basic calibrations include BIAS, DARK and FLAT FIELD
CCD Calibrations
NGC 2736, part of the Vela SN remnant.
Basic calibrations include BIAS, DARK and FLAT FIELD

## Slide 24: CCD Calibrations - Bias
A BIAS frame is a zero-length exposure to show any underlying structure in the image from the CCD or electronics
The bias consists of two components
  a non-varying electronic zero-point level
  plus any structure present
CCD systems usually produce an overscan region to allow the zero-point for each exposure to be measured
The bias structure is a constant and may simply be subtracted from each image
Because of readout noise, average several (say, 10–20) bias frames to create a master bias frame
The image is scaled with only a few ADU from black to white
Little structure is evident
Statistical variation is only 0·4 ADU so this is a clean bias frame
www.sliderbase.com
Notes: CCD Calibrations - Bias
A BIAS frame is a zero-length exposure to show any underlying structure in the image from the CCD or electronics
The bias consists of two components
a non-varying electronic zero-point level
plus any structure present
CCD systems usually produce an overscan region to allow the zero-point for each exposure to be measured
The bias structure is a constant and may simply be subtracted from each image
Because of readout noise, average several (say, 10–20) bias frames to create a master bias frame
The image is scaled with only a few ADU from black to white
Little structure is evident
Statistical variation is only 0·4 ADU so this is a clean bias frame
CCD Calibrations - Bias
A BIAS frame is a zero-length exposure to show any underlying structure in the image from the CCD or electronics
The bias consists of two components
a non-varying electronic zero-point level
plus any structure present
CCD systems usually produce an overscan region to allow the zero-point for each exposure to be measured
The bias structure is a constant and may simply be subtracted from each image
Because of readout noise, average several (say, 10–20) bias frames to create a master bias frame
The image is scaled with only a few ADU from black to white
Little structure is evident
Statistical variation is only 0·4 ADU so this is a clean bias frame

## Slide 25: CCD Calibrations - Dark
To remove dark current, take a series of DARK frames
A dark frame is the same length as a normal exposure but with the shutter closed so no light falls on the CCD
Since CCDs also detect cosmic rays, take several darks and combine them with a median filter to remove cosmic rays from the combined dark frame. Combining several dark frames also minimizes statistical variations.
Subtract the combined dark frame from a normal image, provided they are of the same duration. (After the bias has been removed, of course.)
All images, including darks, contain the bias. A shortcut often used is to not separate out the bias but subtract the dark+bias.
Most research CCDs have very low dark current, so dark frames may not be necessary.
www.sliderbase.com
Notes: To remove dark current, take a series of DARK frames
A dark frame is the same length as a normal exposure but with the shutter closed so no light falls on the CCD
Since CCDs also detect cosmic rays, take several darks and combine them with a median filter to remove cosmic rays from the combined dark frame. Combining several dark frames also minimizes statistical variations.
Subtract the combined dark frame from a normal image, provided they are of the same duration. (After the bias has been removed, of course.)
All images, including darks, contain the bias. A shortcut often used is to not separate out the bias but subtract the dark+bias.
Most research CCDs have very low dark current, so dark frames may not be necessary.
CCD Calibrations - Dark
To remove dark current, take a series of DARK frames
A dark frame is the same length as a normal exposure but with the shutter closed so no light falls on the CCD
Since CCDs also detect cosmic rays, take several darks and combine them with a median filter to remove cosmic rays from the combined dark frame. Combining several dark frames also minimizes statistical variations.
Subtract the combined dark frame from a normal image, provided they are of the same duration. (After the bias has been removed, of course.)
All images, including darks, contain the bias. A shortcut often used is to not separate out the bias but subtract the dark+bias.
Most research CCDs have very low dark current, so dark frames may not be necessary.
CCD Calibrations - Dark

## Slide 26: CCD Calibrations – flat field
Pixel-to-pixel variations are removed with a “flat field” image
A flat field is an image of a featureless, uniform source (such as the twilight sky or a dome projector screen)
A flat field shows the minor pixel variations, as well as all the defects in the optical train (e.g. vignetting and dust spots)
After bias and dark subtraction, divide the image by the “normalized” (image mean reduced to 1.0) flat field
Dividing by the flat field image corrects for variations in sensitivity on the detector and throughput of the telescope and instrument
Center to edge variations and donuts are both are about 1%
www.sliderbase.com
Notes: Pixel-to-pixel variations are removed with a “flat field” image
A flat field is an image of a featureless, uniform source (such as the twilight sky or a dome projector screen)
A flat field shows the minor pixel variations, as well as all the defects in the optical train (e.g. vignetting and dust spots)
After bias and dark subtraction, divide the image by the “normalized” (image mean reduced to 1.0) flat field
Dividing by the flat field image corrects for variations in sensitivity on the detector and throughput of the telescope and instrument
CCD Calibrations – flat field
Center to edge variations and donuts are both are about 1%
Pixel-to-pixel variations are removed with a “flat field” image
A flat field is an image of a featureless, uniform source (such as the twilight sky or a dome projector screen)
A flat field shows the minor pixel variations, as well as all the defects in the optical train (e.g. vignetting and dust spots)
After bias and dark subtraction, divide the image by the “normalized” (image mean reduced to 1.0) flat field
Dividing by the flat field image corrects for variations in sensitivity on the detector and throughput of the telescope and instrument
CCD Calibrations – flat field
Center to edge variations and donuts are both are about 1%

## Slide 27: Flat Field Calibration - Divide (a) by (b) to get (c)
(a)
(b)
(c)
www.sliderbase.com
Notes: Flat Field Calibration - Divide (a) by (b) to get (c)
Flat Field Calibration - Divide (a) by (b) to get (c)

## Slide 28: Cosmic Rays
CCDs are good cosmic ray detectors
Cosmic rays are always found on long exposures
To correct for cosmic rays, take at least three object exposures, and combine them with a median filter
www.sliderbase.com
Notes: Cosmic Rays
CCDs are good cosmic ray detectors
Cosmic rays are always found on long exposures
To correct for cosmic rays, take at least three object exposures, and combine them with a median filter
Cosmic Rays
CCDs are good cosmic ray detectors
Cosmic rays are always found on long exposures
To correct for cosmic rays, take at least three object exposures, and combine them with a median filter

## Slide 29: Other artifacts
poor guiding
donuts
www.sliderbase.com
Notes: Other artifacts
poor guiding
donuts
Other artifacts
poor guiding
donuts

## Slide 30: Data Histograms
A histogram is a plot of the number of times a particular data number occurs vs. data number
www.sliderbase.com
Notes: Data Histograms
A histogram is a plot of the number of times a particular data number occurs vs. data number
Data Histograms
A histogram is a plot of the number of times a particular data number occurs vs. data number

## Slide 31
www.sliderbase.com
Notes: Sources
Kodak KAF-1302E(LE) CCD - Image courtesy of Eastman Kodak Company. KODAK is a trademark. http://www.kodak.com/US/en/digital/ccd/kaf1302ELE.shtml
Other images © Steven Lee http://www.aao.gov.au/local/www/sl/
Bob O'Connell's Fall 2003 Lecture Notes
U. Florida notes on electronic camerasThe_Electronic_Camera_in_Astronomy.ppt
Notes from the Max Planck Institute: http://www.mpia-hd.mpg.de/70CM/lecture/prak_astro.ppt
Sources
Kodak KAF-1302E(LE) CCD - Image courtesy of Eastman Kodak Company. KODAK is a trademark. http://www.kodak.com/US/en/digital/ccd/kaf1302ELE.shtml
Other images © Steven Lee http://www.aao.gov.au/local/www/sl/
Bob O'Connell's Fall 2003 Lecture Notes
U. Florida notes on electronic camerasThe_Electronic_Camera_in_Astronomy.ppt
Notes from the Max Planck Institute: http://www.mpia-hd.mpg.de/70CM/lecture/prak_astro.ppt