## Slide 1: Mass Spectrometry
Courtesy www.lab-initio.com
Notes: Mass Spectrometry

## Slide 2: Purpose of Mass Spectrometry
Produces spectra of masses from the molecules in a sample of material, and fragments of the molecules.
Used to determine
  the elemental composition of a sample
  the masses of particles and of molecules
  potential chemical structures of molecules by analyzing the fragments
  the identity of unknown compounds by determining mass and matching to known spectra
  the isotopic composition of elements in a molecule
Notes: Purpose of Mass Spectrometry
Produces spectra of masses from the molecules in a sample of material, and fragments of the molecules.
Used to determine
the elemental composition of a sample
the masses of particles and of molecules
potential chemical structures of molecules by analyzing the fragments
the identity of unknown compounds by determining mass and matching to known spectra
the isotopic composition of elements in a molecule

## Slide 3: Stages
The ionizer converts some of the sample into ions.
Mass analyzers separate the ions according to their mass-to-charge ratio.
The detector records either the charge induced or the current produced when an ion passes by or hits a surface
Notes: Stages
The ionizer converts some of the sample into ions.
Mass analyzers separate the ions according to their mass-to-charge ratio.
The detector records either the charge induced or the current produced when an ion passes by or hits a surface

## Slide 4: Mass Spectrometry Methods
Ionization method | Typical Analytes | Sample Introduction | Mass Range
Electron Impact (EI) | Relatively small volatile | GC or liquid/solid probe | to 1,000 Daltons
Chemical Ionization (CI) | Relatively small volatile | GC or liquid/solid probe | to 1,000 Daltons
Electrospray (ESI) | Peptides Proteins nonvolatile | Liquid Chromatography or syringe | to 200,000 Daltons
Fast Atom Bombardment (FAB) | Carbohydrates Organometallics Peptides nonvolatile | Sample mixed in viscous matrix | to 6,000 Daltons
Matrix Assisted Laser Desorption (MALDI) | Peptides Proteins Nucleotides | Sample mixed in solid matrix | to 500,000 Daltons
http://www.chem.arizona.edu/massspec/intro_html/intro.html
Notes: Mass Spectrometry Methods
http://www.chem.arizona.edu/massspec/intro_html/intro.html

## Slide 5: Mass Spectrum of CO2
Molecular ion peak
[CO2]+ = 44
[CO]+ = 28
[O]+ = 16
[C]+ = 12
Fragment Peaks
Notes: Mass Spectrum of CO2
Molecular ion peak
[CO2]+ = 44
[CO]+ = 28
[O]+ = 16
[C]+ = 12
Fragment Peaks

## Slide 6: Mass Spectrum of Bromine, Br2
Bromine has two isotopes: 50.69% 79Br and 49.31% 81Br
79Br+
81Br+
[79Br81Br]+
[79Br79Br]+
[81Br81Br]+
Molecular Ion Peaks
Fragments
Notes: Mass Spectrum of Bromine, Br2
Bromine has two isotopes: 50.69% 79Br and 49.31% 81Br
79Br+
81Br+
[79Br81Br]+
[79Br79Br]+
[81Br81Br]+
Molecular Ion Peaks
Fragments

## Slide 7: Practice: Methyl Bromide, CH3Br
Notes: Practice: Methyl Bromide, CH3Br

## Slide 8: Answers: Methyl Bromide, CH3Br
[CH381Br]+
[CH281Br]+
[C81Br]+ and [CH279Br]+
[CH81Br]+ and [CH379Br]+
[CH79Br]+
[CH3]+
[C79Br]+
[81Br]+
[79Br]+
Notes: Answers: Methyl Bromide, CH3Br
[CH381Br]+
[CH281Br]+
[C81Br]+ and [CH279Br]+
[CH81Br]+ and [CH379Br]+
[CH79Br]+
[CH3]+
[C79Br]+
[81Br]+
[79Br]+

## Slide 9: Practice: Methylene Chloride (CH2Cl2)
Chlorine is 75.77% 35Cl and 24.23% 37Cl
Notes: Practice: Methylene Chloride (CH2Cl2)
Chlorine is 75.77% 35Cl and 24.23% 37Cl

## Slide 10: Practice: Vinyl Chloride (CH2CHCl)
Chlorine is 75.77% 35Cl and 24.23% 37Cl
Notes: Practice: Vinyl Chloride (CH2CHCl)
Chlorine is 75.77% 35Cl and 24.23% 37Cl

## Slide 11: Spectra of Larger Molecules
Spectra of large molecules have many fragments, and the interpretation of their spectra is beyond the scope of this course.
Codeine, C18H21NO3
Notes: Spectra of Larger Molecules
Spectra of large molecules have many fragments, and the interpretation of their spectra is beyond the scope of this course.
Codeine, C18H21NO3

## Slide 12: Toluene ( C7H8) Fragmentation
**Note that the molecular ion peak is NOT the dominant peak in the spectrum
Notes: Toluene ( C7H8) Fragmentation
**Note that the molecular ion peak is NOT the dominant peak in the spectrum

## Slide 13: Mass Spectrometry in Forensics
Mass spectrometry is used to confirm the identify of unknowns, such as illegal drugs
Unknowns are often not pure, and must be separated from a mixture
Gas chromatography is used to separate the components of the mixture
Mass spectrometry “fingerprints” the components, so that they can be matched to existing known spectra
Gas
Chromatograph
Mixture
Mass
Spectrometer
Notes: Mass Spectrometry in Forensics
Mass spectrometry is used to confirm the identify of unknowns, such as illegal drugs
Unknowns are often not pure, and must be separated from a mixture
Gas chromatography is used to separate the components of the mixture
Mass spectrometry “fingerprints” the components, so that they can be matched to existing known spectra
Gas
Chromatograph
Mixture
Mass
Spectrometer