## Slide 1: The Lecture Series
1st Lecture: 9/30/05, 2:00 pm: Definitions, Formalism, Examples
2nd Lecture: 10/7/05, 2:00 pm: Ion-optical elements, properties & design
3rd Lecture: 10/14/05, 2:00 pm: Real World Ion-optical Systems
4th Lecture: 12/2/05, 2:00 pm: Separator Systems
5th Lecture: 12/9/05, 2:00 pm: Demonstration of Codes (TRANSPORT, COSY, MagNet)
www.sliderbase.com
Notes: The Lecture Series
1st Lecture: 9/30/05, 2:00 pm: Definitions, Formalism, Examples
2nd Lecture: 10/7/05, 2:00 pm: Ion-optical elements, properties & design
3rd Lecture: 10/14/05, 2:00 pm: Real World Ion-optical Systems
4th Lecture: 12/2/05, 2:00 pm: Separator Systems
5th Lecture: 12/9/05, 2:00 pm: Demonstration of Codes (TRANSPORT, COSY, MagNet)
www.sliderbase.com
The Lecture Series
1st Lecture: 9/30/05, 2:00 pm: Definitions, Formalism, Examples
2nd Lecture: 10/7/05, 2:00 pm: Ion-optical elements, properties & design
3rd Lecture: 10/14/05, 2:00 pm: Real World Ion-optical Systems
4th Lecture: 12/2/05, 2:00 pm: Separator Systems
5th Lecture: 12/9/05, 2:00 pm: Demonstration of Codes (TRANSPORT, COSY, MagNet)
www.sliderbase.com

## Slide 2: 1st Lecture
Motivation, references, remarks (4 - 8)
The driving forces (9)
Definitions & first order formalism (10 - 16)
Phase space ellipse, emittance, examples (17 - 25)
Taylor expansion, higher orders (26 - 27)
The power of diagnostics (28 - 30)
Q & A
1st Lecture: 9/30/05, 2:00 – 3:30 pm: Definitions, Formalism, Examples
www.sliderbase.com
Notes: 1st Lecture
Motivation, references, remarks (4 - 8)
The driving forces (9)
Definitions & first order formalism (10 - 16)
Phase space ellipse, emittance, examples (17 - 25)
Taylor expansion, higher orders (26 - 27)
The power of diagnostics (28 - 30)
Q & A
1st Lecture: 9/30/05, 2:00 – 3:30 pm: Definitions, Formalism, Examples
www.sliderbase.com
1st Lecture
Motivation, references, remarks (4 - 8)
The driving forces (9)
Definitions & first order formalism (10 - 16)
Phase space ellipse, emittance, examples (17 - 25)
Taylor expansion, higher orders (26 - 27)
The power of diagnostics (28 - 30)
Q & A
1st Lecture: 9/30/05, 2:00 – 3:30 pm: Definitions, Formalism, Examples
www.sliderbase.com

## Slide 3: Motivation
Manipulate charged particles (, ions, like p,d,…)
Beam lines systems
Magnetic & electric analysis/ separation (e.g. St. George)
Acceleration of ions
www.sliderbase.com
Notes: Motivation
Manipulate charged particles (b+/-, ions, like p,d,a, …)
Beam lines systems
Magnetic & electric analysis/ separation (e.g. St. George)
Acceleration of ions
www.sliderbase.com
Motivation
Manipulate charged particles (b+/-, ions, like p,d,a, …)
Beam lines systems
Magnetic & electric analysis/ separation (e.g. St. George)
Acceleration of ions
www.sliderbase.com

## Slide 4: Who needs ion-optics anyway?
Over 6*109 people have - I hope so - happy lives without!
A group of accelerator physicists are using it to build machines
that enables physicists to explore the unkown!
Many physicists using accelerators, beam lines and magnet system
(or their data) needs some knowledge of ion-optics.
This lecture series is an introduction to the last group and I will do
my best to let you in on the basics first and than we will discuss
some of the applications of ion-optics and related topics.
www.sliderbase.com
Notes: Who needs ion-optics anyway?
Over 6*109 people have - I hope so - happy lives without!
A group of accelerator physicists are using it to build machines
that enables physicists to explore the unkown!
Many physicists using accelerators, beam lines and magnet system
(or their data) needs some knowledge of ion-optics.
This lecture series is an introduction to the last group and I will do
my best to let you in on the basics first and than we will discuss
some of the applications of ion-optics and related topics.
www.sliderbase.com
Who needs ion-optics anyway?
Over 6*109 people have - I hope so - happy lives without!
A group of accelerator physicists are using it to build machines
that enables physicists to explore the unkown!
Many physicists using accelerators, beam lines and magnet system
(or their data) needs some knowledge of ion-optics.
This lecture series is an introduction to the last group and I will do
my best to let you in on the basics first and than we will discuss
some of the applications of ion-optics and related topics.
www.sliderbase.com

## Slide 5: Introductory remarks
Introduction for physicists  Focus on ion-optical definitions, and tools that
are useful for physicist at the NSL & future users of St. George recoil separator.
Light optics can hardly be discussed without lenses & optical instruments
 ion-optics requires knowledge of ion-optical elements.
Analogy between Light Optics and Ion-Optics is useful but limited.
Ion-optical & magnet design tools needed to understand electro-magnet systems. Ion-optics is not even 100 years old and (still) less intuitive than optics developed
since several hundred years
Galileo
Telescope 1609 
 Optics in Siderus Nuncius 1610
Historical remarks: Rutherford, 1911, discovery of atomic nucleus
www.sliderbase.com
Notes: Introductory remarks
Introduction for physicists  Focus on ion-optical definitions, and tools that
are useful for physicist at the NSL & future users of St. George recoil separator.
Light optics can hardly be discussed without lenses & optical instruments
 ion-optics requires knowledge of ion-optical elements.
Analogy between Light Optics and Ion-Optics is useful but limited.
Ion-optical & magnet design tools needed to understand electro-magnet systems. Ion-optics is not even 100 years old and (still) less intuitive than optics developed
since several hundred years
Galileo
Telescope 1609 
 Optics in Siderus Nuncius 1610
Historical remarks: Rutherford, 1911, discovery of atomic nucleus
www.sliderbase.com
Introductory remarks
Introduction for physicists  Focus on ion-optical definitions, and tools that
are useful for physicist at the NSL & future users of St. George recoil separator.
Light optics can hardly be discussed without lenses & optical instruments
 ion-optics requires knowledge of ion-optical elements.
Analogy between Light Optics and Ion-Optics is useful but limited.
Ion-optical & magnet design tools needed to understand electro-magnet systems. Ion-optics is not even 100 years old and (still) less intuitive than optics developed
since several hundred years
Galileo
Telescope 1609 
 Optics in Siderus Nuncius 1610
Historical remarks: Rutherford, 1911, discovery of atomic nucleus
www.sliderbase.com

## Slide 6: Basic tools of the trade
Geometry, drawing tools, CAD drafting program (e.g. AutoCad)
Linear Algebra (Matrix calculations), first order ion-optics (e.g. TRANSPORT)
Higher order ion-optics code to solve equation of motion, (e.g. COSY Infinity,
GIOS, RAYTRACE (historic)
Electro-magnetic field program (solution of Maxwell’s Equations),
(e.g. finite element (FE) codes, 2d & 3d: POISSON, TOSCA, MagNet)
Properties of incoming charged particles and design function of electro-magnetic
facility, beam, reaction products (e.g. kinematic codes, charge distributions of
heavy ions, energy losses in targets)
Many other specialized programs, e.g for accelerator design (e.g. synchrotrons,
cyclotrons) not covered in this lecure series.
www.sliderbase.com
Notes: Basic tools of the trade
Geometry, drawing tools, CAD drafting program (e.g. AutoCad)
Linear Algebra (Matrix calculations), first order ion-optics (e.g. TRANSPORT)
Higher order ion-optics code to solve equation of motion, (e.g. COSY Infinity,
GIOS, RAYTRACE (historic)
Electro-magnetic field program (solution of Maxwell’s Equations),
(e.g. finite element (FE) codes, 2d & 3d: POISSON, TOSCA, MagNet)
Properties of incoming charged particles and design function of electro-magnetic
facility, beam, reaction products (e.g. kinematic codes, charge distributions of
heavy ions, energy losses in targets)
Many other specialized programs, e.g for accelerator design (e.g. synchrotrons,
cyclotrons) not covered in this lecure series.
www.sliderbase.com
Basic tools of the trade
Geometry, drawing tools, CAD drafting program (e.g. AutoCad)
Linear Algebra (Matrix calculations), first order ion-optics (e.g. TRANSPORT)
Higher order ion-optics code to solve equation of motion, (e.g. COSY Infinity,
GIOS, RAYTRACE (historic)
Electro-magnetic field program (solution of Maxwell’s Equations),
(e.g. finite element (FE) codes, 2d & 3d: POISSON, TOSCA, MagNet)
Properties of incoming charged particles and design function of electro-magnetic
facility, beam, reaction products (e.g. kinematic codes, charge distributions of
heavy ions, energy losses in targets)
Many other specialized programs, e.g for accelerator design (e.g. synchrotrons,
cyclotrons) not covered in this lecure series.
www.sliderbase.com

## Slide 7: Literature
Optics of Charged Particles, Hermann Wollnik, Academic Press, Orlando, 1987
The Optics of Charged Particle Beams, David.C Carey, Harwood Academic
Publishers, New York 1987
Accelerator Physics, S.Y. Lee, World Scientific Publishing, Singapore, 1999
TRANSPORT, A Computer Program for Designing Charged Particle Beam
Transport Systems, K.L. Brown, D.C. Carey, Ch. Iselin, F. Rotacker,
Report CERN 80-04, Geneva, 1980
Computer-Aided Design in Magnetics, D.A. Lowther, P. Silvester, Springer 1985
www.sliderbase.com
Notes: Literature
Optics of Charged Particles, Hermann Wollnik, Academic Press, Orlando, 1987
The Optics of Charged Particle Beams, David.C Carey, Harwood Academic
Publishers, New York 1987
Accelerator Physics, S.Y. Lee, World Scientific Publishing, Singapore, 1999
TRANSPORT, A Computer Program for Designing Charged Particle Beam
Transport Systems, K.L. Brown, D.C. Carey, Ch. Iselin, F. Rotacker,
Report CERN 80-04, Geneva, 1980
Computer-Aided Design in Magnetics, D.A. Lowther, P. Silvester, Springer 1985
www.sliderbase.com
Literature
Optics of Charged Particles, Hermann Wollnik, Academic Press, Orlando, 1987
The Optics of Charged Particle Beams, David.C Carey, Harwood Academic
Publishers, New York 1987
Accelerator Physics, S.Y. Lee, World Scientific Publishing, Singapore, 1999
TRANSPORT, A Computer Program for Designing Charged Particle Beam
Transport Systems, K.L. Brown, D.C. Carey, Ch. Iselin, F. Rotacker,
Report CERN 80-04, Geneva, 1980
Computer-Aided Design in Magnetics, D.A. Lowther, P. Silvester, Springer 1985
www.sliderbase.com

## Slide 8: Ions in static or quasi-static electro-magnetic fields
Lorentz Force
q = electric charge
B = magn. induction
E = electric field
v = velocity
For momentum analysis the magnetic force is preferred because the force is always perpendicular to B. Therefore v, p and E are constant.
Force in magnetic dipole B = const: p = q B 
p = mv = momentum
= bending radius
= magn. rigidity
For ion acceleration electric forces are used.
Dipole field B
perpendicular
to paper plane
Radius
Object (size x0)

General rule:
Scaling of magnetic system
in the linear region results
in the same ion-optics
Note: Dispersion x/p
used in magnetic analysis,
e.g. Spectrometers, magn.
Separators,
x
p
p+p
(1)
www.sliderbase.com
Notes: Ions in static or quasi-static electro-magnetic fields
Lorentz Force
q = electric charge
B = magn. induction
E = electric field
v = velocity
For momentum analysis the magnetic force is preferred because the force is always perpendicular to B. Therefore v, p and E are constant.
Force in magnetic dipole B = const: p = q B r
p = mv = momentum
= bending radius
Br = magn. rigidity
For ion acceleration electric forces are used.
Dipole field B
perpendicular
to paper plane
Radius r
Object (size x0)
General rule:
Scaling of magnetic system
in the linear region results
in the same ion-optics
Note: Dispersion dx/dp
used in magnetic analysis,
e.g. Spectrometers, magn.
Separators,
x
p
p+dp
(1)
www.sliderbase.com
Ions in static or quasi-static electro-magnetic fields
Lorentz Force
q = electric charge
B = magn. induction
E = electric field
v = velocity
For momentum analysis the magnetic force is preferred because the force is always perpendicular to B. Therefore v, p and E are constant.
Force in magnetic dipole B = const: p = q B r
p = mv = momentum
= bending radius
Br = magn. rigidity
For ion acceleration electric forces are used.
Dipole field B
perpendicular
to paper plane
Radius r
Object (size x0)
General rule:
Scaling of magnetic system
in the linear region results
in the same ion-optics
Note: Dispersion dx/dp
used in magnetic analysis,
e.g. Spectrometers, magn.
Separators,
x
p
p+dp
(1)
www.sliderbase.com

## Slide 9: Definition of BEAM for mathematical formulation of ion-optics
What is a beam, what shapes it,
how do we know its properties ?
Beam parameters, the long list
Beam rays and distributions
Beam line elements, paraxial lin. approx.
higher orders in spectrometers
System of diagnostic instruments
Not to forget: Atomic charge Q
Number of particles n
www.sliderbase.com
Notes: Definition of BEAM for mathematical formulation of ion-optics
What is a beam, what shapes it,
how do we know its properties ?
Beam parameters, the long list
Beam rays and distributions
Beam line elements, paraxial lin. approx.
higher orders in spectrometers
System of diagnostic instruments
Not to forget: Atomic charge Q
Number of particles n
www.sliderbase.com
Definition of BEAM for mathematical formulation of ion-optics
What is a beam, what shapes it,
how do we know its properties ?
Beam parameters, the long list
Beam rays and distributions
Beam line elements, paraxial lin. approx.
higher orders in spectrometers
System of diagnostic instruments
Not to forget: Atomic charge Q
Number of particles n
www.sliderbase.com

## Slide 10: Defining a RAY
Ion-optical
element
Code TRANSPORT:
(x, y,1dp/p)
(1, 2, 3, 4, 5, 6 )
Convenient “easy to use” program
for beam lines with paraxial beams
Code: COSY Infinity:
(x, ay, b, l, K, m, z)
Needed for complex ion-optical systems including several
charge states
different masses
velocities (e.g. Wien Filter)
higher order corrections
Not defined in the figure are:
KdK/K = rel. energy
mdm/m = rel. energy
z = dq/q = rel. charge change
a = px/p0
b = py/p0
All parameters are relative
to “central ray” properties
Not defined in the figure are:
dp/p = rel. momentum
l = beam pulse length
All parameters are relative
to “central ray”
central ray
Note: Notations in the Literature is not consistent! Sorry, neither will I be.
www.sliderbase.com
Notes: Defining a RAY
Ion-optical
element
Code TRANSPORT:
(x, Q, y, F, 1, dp/p)
(1, 2, 3, 4, 5, 6 )
Convenient “easy to use” program
for beam lines with paraxial beams
Code: COSY Infinity:
(x, a, y, b, l, dK, dm, dz)
Needed for complex ion-optical systems including several
charge states
different masses
velocities (e.g. Wien Filter)
higher order corrections
Not defined in the figure are:
dK = dK/K = rel. energy
dm = dm/m = rel. energy
dz = dq/q = rel. charge change
a = px/p0
b = py/p0
All parameters are relative
to “central ray” properties
Not defined in the figure are:
dp/p = rel. momentum
l = beam pulse length
All parameters are relative
to “central ray”
central ray
Note: Notations in the Literature is not consistent! Sorry, neither will I be.
www.sliderbase.com
Defining a RAY
Ion-optical
element
Code TRANSPORT:
(x, Q, y, F, 1, dp/p)
(1, 2, 3, 4, 5, 6 )
Convenient “easy to use” program
for beam lines with paraxial beams
Code: COSY Infinity:
(x, a, y, b, l, dK, dm, dz)
Needed for complex ion-optical systems including several
charge states
different masses
velocities (e.g. Wien Filter)
higher order corrections
Not defined in the figure are:
dK = dK/K = rel. energy
dm = dm/m = rel. energy
dz = dq/q = rel. charge change
a = px/p0
b = py/p0
All parameters are relative
to “central ray” properties
Not defined in the figure are:
dp/p = rel. momentum
l = beam pulse length
All parameters are relative
to “central ray”
central ray
Note: Notations in the Literature is not consistent! Sorry, neither will I be.
www.sliderbase.com

## Slide 11: TRANSPORT Coordinate System
Ray at initial
Location 1


www.sliderbase.com
Notes: Ray at initial
Location 1


TRANSPORT Coordinate System
www.sliderbase.com
Ray at initial
Location 1


TRANSPORT Coordinate System
www.sliderbase.com

## Slide 12: Transport of a ray
Ray at initial
Location 0
Ray after element at
Location t


6x6 Matrix
representing
optic element
(first order)

Note: We are not building “random” optical elements.
Many matrix elements = 0
because of symmetries, e.g. mid-plane symmetry
(2)
www.sliderbase.com
Notes: Transport of a ray
Ray at initial
Location 0
Ray after element at
Location t


6x6 Matrix
representing
optic element
(first order)

Note: We are not building “random” optical elements.
Many matrix elements = 0
because of symmetries, e.g. mid-plane symmetry
(2)
www.sliderbase.com
Transport of a ray
Ray at initial
Location 0
Ray after element at
Location t


6x6 Matrix
representing
optic element
(first order)

Note: We are not building “random” optical elements.
Many matrix elements = 0
because of symmetries, e.g. mid-plane symmetry
(2)
www.sliderbase.com

## Slide 13: TRANSPORT matrices of a Drift and a Quadrupole
For reference of TRANSPORT code and formalism:
K.L. Brown, F. Rothacker, D.C. Carey, and Ch. Iselin,
TRANSPORT: A computer program for designing
charged particle beam transport systems, SLAC-91,
Rev. 2, UC-28 (I/A), also: CERN 80-04 Super Proton
Synchrotron Division, 18 March 1980, Geneva,
Manual plus Appendices available on Webpage:
ftp://ftp.psi.ch/psi/transport.beam/CERN-80-04/
David. C. Carey, The optics of Charged Particle Beams,
1987, Hardwood Academic Publ. GmbH, Chur Switzerland
www.sliderbase.com
Notes: TRANSPORT matrices of a Drift and a Quadrupole
For reference of TRANSPORT code and formalism:
K.L. Brown, F. Rothacker, D.C. Carey, and Ch. Iselin,
TRANSPORT: A computer program for designing
charged particle beam transport systems, SLAC-91,
Rev. 2, UC-28 (I/A), also: CERN 80-04 Super Proton
Synchrotron Division, 18 March 1980, Geneva,
Manual plus Appendices available on Webpage:
ftp://ftp.psi.ch/psi/transport.beam/CERN-80-04/
David. C. Carey, The optics of Charged Particle Beams,
1987, Hardwood Academic Publ. GmbH, Chur Switzerland
www.sliderbase.com
TRANSPORT matrices of a Drift and a Quadrupole
For reference of TRANSPORT code and formalism:
K.L. Brown, F. Rothacker, D.C. Carey, and Ch. Iselin,
TRANSPORT: A computer program for designing
charged particle beam transport systems, SLAC-91,
Rev. 2, UC-28 (I/A), also: CERN 80-04 Super Proton
Synchrotron Division, 18 March 1980, Geneva,
Manual plus Appendices available on Webpage:
ftp://ftp.psi.ch/psi/transport.beam/CERN-80-04/
David. C. Carey, The optics of Charged Particle Beams,
1987, Hardwood Academic Publ. GmbH, Chur Switzerland
www.sliderbase.com

## Slide 14: Transport of a ray though a system of beam line elements
Ray at initial
Location 0
(e.g. a target)
Ray at final
Location n


6x6 Matrix
representing
first optic element
(usually a Drift)

xn = Rn Rn-1 … R0 x0
Complete system is represented by
one Matrix Rsystem = Rn Rn-1 … R0
(3)
(4)
www.sliderbase.com
Notes: Transport of a ray though a system of beam line elements
Ray at initial
Location 0
(e.g. a target)
Ray at final
Location n


6x6 Matrix
representing
first optic element
(usually a Drift)

xn = Rn Rn-1 … R0 x0
Complete system is represented by
one Matrix Rsystem = Rn Rn-1 … R0
(3)
(4)
www.sliderbase.com
Transport of a ray though a system of beam line elements
Ray at initial
Location 0
(e.g. a target)
Ray at final
Location n


6x6 Matrix
representing
first optic element
(usually a Drift)

xn = Rn Rn-1 … R0 x0
Complete system is represented by
one Matrix Rsystem = Rn Rn-1 … R0
(3)
(4)
www.sliderbase.com

## Slide 15: Geometrical interpretation of some TRANSPORT matrix elements
Wollnik, p. 16
Focusing Function
(x|a) Wollnik
= dx/d physical meaning
= (x|) RAYTRACE
= R12 TRANSPORT
Achromatic system:
R16 = R26 = 0
www.sliderbase.com
Notes: Geometrical interpretation of some TRANSPORT matrix elements
Wollnik, p. 16
Focusing Function
(x|a) Wollnik
= dx/dQ physical meaning
= (x|Q) RAYTRACE
= R12 TRANSPORT
Achromatic system:
R16 = R26 = 0
www.sliderbase.com
Geometrical interpretation of some TRANSPORT matrix elements
Wollnik, p. 16
Focusing Function
(x|a) Wollnik
= dx/dQ physical meaning
= (x|Q) RAYTRACE
= R12 TRANSPORT
Achromatic system:
R16 = R26 = 0
www.sliderbase.com

## Slide 16: Defining a BEAM
(Ellipse Area = (det )1/2
Emittance  is constant for
fixed energy & conservative
forces (Liouville’s Theorem)
Note:  shrinks (increases) with acceleration (deceleration); Dissipative forces:  increases in gases; electron, stochastic, laser cooling
Attention:
Space charge effects occur when the particle density is high, so that particles repel each other
Warning:
This is a mathematical abstraction of a beam:
It is your responsibility to verify it applies to your beam
2 dimensional cut x- is shown

 - (

Emittance
(5)
www.sliderbase.com
Notes: Defining a BEAM
(Ellipse Area = p(det s)1/2
Emittance e is constant for
fixed energy & conservative
forces (Liouville’s Theorem)
Note: e shrinks (increases) with acceleration (deceleration); Dissipative forces: e increases in gases; electron, stochastic, laser cooling
Attention:
Space charge effects occur when the particle density is high, so that particles repel each other
Warning:
This is a mathematical abstraction of a beam:
It is your responsibility to verify it applies to your beam
2 dimensional cut x-Q is shown
e = Ö
s11s22 - (s12) 2
```````````
Emittance
(5)
www.sliderbase.com
Defining a BEAM
(Ellipse Area = p(det s)1/2
Emittance e is constant for
fixed energy & conservative
forces (Liouville’s Theorem)
Note: e shrinks (increases) with acceleration (deceleration); Dissipative forces: e increases in gases; electron, stochastic, laser cooling
Attention:
Space charge effects occur when the particle density is high, so that particles repel each other
Warning:
This is a mathematical abstraction of a beam:
It is your responsibility to verify it applies to your beam
2 dimensional cut x-Q is shown
e = Ö
s11s22 - (s12) 2
```````````
Emittance
(5)
www.sliderbase.com

## Slide 17: Equivalence of Transport of ONE Ray Ellipse
Defining the  Matrix representing a Beam
www.sliderbase.com
Notes: Equivalence of Transport of ONE Ray Û Ellipse
Defining the s Matrix representing a Beam
www.sliderbase.com
Equivalence of Transport of ONE Ray Û Ellipse
Defining the s Matrix representing a Beam
www.sliderbase.com

## Slide 18: The 2-dimensional case ( x,  )
Ellipse Area = (det )1/2
Emittance  = det  is constant
for fixed energy & conservative
forces (Liouville’s Theorem)
Note:  shrinks (increases) with acceleration (deceleration); Dissipative forces:  increases in gases; electron, stochastic, laser cooling
2 dimensional cut x- is shown



Real, pos. definite
symmetric  Matrix



Inverse Matrix



Exercise 1:
Show that:
= I (Unity Matrix)
2-dim. Coord.vectors
(point in phase space)
X =
X T = (x )
x

Ellipse in Matrix notation:
X T  X = 1
Exercise 2: Show that Matrix notation
is equivalent to known Ellipse equation:
 x2x = 2
(6)
www.sliderbase.com
Notes: The 2-dimensional case ( x, Q )
Ellipse Area = p(det s)1/2
Emittance e = det s is constant
for fixed energy & conservative
forces (Liouville’s Theorem)
Note: e shrinks (increases) with acceleration (deceleration); Dissipative forces: e increases in gases; electron, stochastic, laser cooling
2 dimensional cut x-Q is shown
s =
æs11 s21 ü
ès21 s22 þ
Real, pos. definite
symmetric s Matrix
s-1 = 1/e2
æs22 -s21 ü
è-s21 s11 þ
Inverse Matrix
ss-1 =
æ1 0 ü
è 0 1þ
Exercise 1:
Show that:
= I (Unity Matrix)
2-dim. Coord.vectors
(point in phase space)
X =
X T = (x Q)
æx ü
èQþ
Ellipse in Matrix notation:
X T s-1 X = 1
Exercise 2: Show that Matrix notation
is equivalent to known Ellipse equation:
s22 x2 - 2s21 x Q + s11Q2 = e2
(6)
www.sliderbase.com
The 2-dimensional case ( x, Q )
Ellipse Area = p(det s)1/2
Emittance e = det s is constant
for fixed energy & conservative
forces (Liouville’s Theorem)
Note: e shrinks (increases) with acceleration (deceleration); Dissipative forces: e increases in gases; electron, stochastic, laser cooling
2 dimensional cut x-Q is shown
s =
æs11 s21 ü
ès21 s22 þ
Real, pos. definite
symmetric s Matrix
s-1 = 1/e2
æs22 -s21 ü
è-s21 s11 þ
Inverse Matrix
ss-1 =
æ1 0 ü
è 0 1þ
Exercise 1:
Show that:
= I (Unity Matrix)
2-dim. Coord.vectors
(point in phase space)
X =
X T = (x Q)
æx ü
èQþ
Ellipse in Matrix notation:
X T s-1 X = 1
Exercise 2: Show that Matrix notation
is equivalent to known Ellipse equation:
s22 x2 - 2s21 x Q + s11Q2 = e2
(6)
www.sliderbase.com

## Slide 19: Courant-Snyder Notation



In their famous “Theory of the Alternating Synchrotron” Courant and Snyder used a
Different notation of the  Matrix Elements, that are used in the Accelerator Literature.
For you r future venture into accelerator physics here is the relationship between the
 matrix and the betatron amplitue functions  or Courant Snyder parameters



www.sliderbase.com
Notes: Courant-Snyder Notation
s =
æs11 s21 ü
ès21 s22 þ
In their famous “Theory of the Alternating Synchrotron” Courant and Snyder used a
Different notation of the s Matrix Elements, that are used in the Accelerator Literature.
For you r future venture into accelerator physics here is the relationship between the
s matrix and the betatron amplitue functions a, b, g or Courant Snyder parameters
æ b -a ü
è-a g þ
= e
www.sliderbase.com
Courant-Snyder Notation
s =
æs11 s21 ü
ès21 s22 þ
In their famous “Theory of the Alternating Synchrotron” Courant and Snyder used a
Different notation of the s Matrix Elements, that are used in the Accelerator Literature.
For you r future venture into accelerator physics here is the relationship between the
s matrix and the betatron amplitue functions a, b, g or Courant Snyder parameters
æ b -a ü
è-a g þ
= e
www.sliderbase.com

## Slide 20: Transport of 6-dim  Matrix
Consider the 6-dim. ray vector in TRANSPORT: X = (x, y,l, dp/p)
Ray X0 from location 0 is transported by a 6 x 6 Matrix R to location 1 by: X1 = RX0
Note: R maybe a matrix representing a complex system (3) is : R = Rn Rn-1 … R0
Ellipsoid in Matrix notation (6), generized to e.g. 6-dim. using  Matrix: X0 T  X0 = 1
Inserting Unity Matrix I = RR-1 in equ. (6) it follows X0 T (RTRT-1) (R-1 R) X0 = 1
from which we derive (RX0)T (RRT)-1 (RX0) = 1
(7)
(9)
(8)
The equation of the new ellipsoid after transformation becomes X1 T  X1 = 1
where  = RRT
(10)
(6)
Conclusion: Knowing the TRANSPORT matrix R that transports one ray through an ion-optical system using (7) we can now also transport the phase space ellipse describing the initial beam using (10)
www.sliderbase.com
Notes: Transport of 6-dim s Matrix
Consider the 6-dim. ray vector in TRANSPORT: X = (x, Q, y, F, l, dp/p)
Ray X0 from location 0 is transported by a 6 x 6 Matrix R to location 1 by: X1 = RX0
Note: R maybe a matrix representing a complex system (3) is : R = Rn Rn-1 … R0
Ellipsoid in Matrix notation (6), generized to e.g. 6-dim. using s Matrix: X0 T s0-1 X0 = 1
Inserting Unity Matrix I = RR-1 in equ. (6) it follows X0 T (RTRT-1) s0-1 (R-1 R) X0 = 1
from which we derive (RX0)T (Rs0 RT)-1 (RX0) = 1
(7)
(9)
(8)
The equation of the new ellipsoid after transformation becomes X1 T s1-1 X1 = 1
where s1 = Rs0 RT
(10)
(6)
Conclusion: Knowing the TRANSPORT matrix R that transports one ray through an ion-optical system using (7) we can now also transport the phase space ellipse describing the initial beam using (10)
www.sliderbase.com
Transport of 6-dim s Matrix
Consider the 6-dim. ray vector in TRANSPORT: X = (x, Q, y, F, l, dp/p)
Ray X0 from location 0 is transported by a 6 x 6 Matrix R to location 1 by: X1 = RX0
Note: R maybe a matrix representing a complex system (3) is : R = Rn Rn-1 … R0
Ellipsoid in Matrix notation (6), generized to e.g. 6-dim. using s Matrix: X0 T s0-1 X0 = 1
Inserting Unity Matrix I = RR-1 in equ. (6) it follows X0 T (RTRT-1) s0-1 (R-1 R) X0 = 1
from which we derive (RX0)T (Rs0 RT)-1 (RX0) = 1
(7)
(9)
(8)
The equation of the new ellipsoid after transformation becomes X1 T s1-1 X1 = 1
where s1 = Rs0 RT
(10)
(6)
Conclusion: Knowing the TRANSPORT matrix R that transports one ray through an ion-optical system using (7) we can now also transport the phase space ellipse describing the initial beam using (10)
www.sliderbase.com

## Slide 21: The transport of rays and phase ellipses in a Drift and focusing Quadrupole, Lens
2.
3.
Matching of emittance and acceptance
Lens 2
Lens 3
Focus
Focus
www.sliderbase.com
Notes: The transport of rays and phase ellipses in a Drift and focusing Quadrupole, Lens
2.
3.
Matching of emittance and acceptance
Lens 2
Lens 3
Focus
Focus
www.sliderbase.com
The transport of rays and phase ellipses in a Drift and focusing Quadrupole, Lens
2.
3.
Matching of emittance and acceptance
Lens 2
Lens 3
Focus
Focus
www.sliderbase.com

## Slide 22: Increase of Emittance  due to degrader
Focus
A degrader / target increases the
emittance  due to multiple scattering.
The emittance growth is minimal when
the degrader in positioned in a focus
As can be seen from the schematic
drawing of the horizontal x-Theta
Phase space.
for back-of-the-envelop discussions!
www.sliderbase.com
Notes: Increase of Emittance e due to degrader
Focus
A degrader / target increases the
emittance e due to multiple scattering.
The emittance growth is minimal when
the degrader in positioned in a focus
As can be seen from the schematic
drawing of the horizontal x-Theta
Phase space.
for back-of-the-envelop discussions!
www.sliderbase.com
Increase of Emittance e due to degrader
Focus
A degrader / target increases the
emittance e due to multiple scattering.
The emittance growth is minimal when
the degrader in positioned in a focus
As can be seen from the schematic
drawing of the horizontal x-Theta
Phase space.
for back-of-the-envelop discussions!
www.sliderbase.com

## Slide 23: Emittance  measurement by tuning a quadrupole
Lee, p. 55
The emittance  is an important
parameter of a beam. It can be measured as shown below.
 L/L gL)/
xmax =
Exercise 3:
In the accelerator
reference book 22 is printed as 
Verify which is correct
Bz/x  l
B
g =
(Quadr. field strength
l = eff. field length)
L = Distance between quadrupole and
beam profile monitor
Take minimum 3 measurements of
xmax(g) and determine Emittance 
(11)
(12)
www.sliderbase.com
Notes: Emittance e measurement by tuning a quadrupole
Lee, p. 55
The emittance e is an important
parameter of a beam. It can be measured as shown below.
s11 (1 + s12 L/ s11 - L g) + (eL)2/s22
xmax =
Exercise 3:
In the accelerator
reference book s22 is printed as s11
Verify which is correct
¶Bz/¶x * l
Br
g =
(Quadr. field strength
l = eff. field length)
L = Distance between quadrupole and
beam profile monitor
Take minimum 3 measurements of
xmax(g) and determine Emittance e
(11)
(12)
www.sliderbase.com
Emittance e measurement by tuning a quadrupole
Lee, p. 55
The emittance e is an important
parameter of a beam. It can be measured as shown below.
s11 (1 + s12 L/ s11 - L g) + (eL)2/s22
xmax =
Exercise 3:
In the accelerator
reference book s22 is printed as s11
Verify which is correct
¶Bz/¶x * l
Br
g =
(Quadr. field strength
l = eff. field length)
L = Distance between quadrupole and
beam profile monitor
Take minimum 3 measurements of
xmax(g) and determine Emittance e
(11)
(12)
www.sliderbase.com

## Slide 24: Emittance  measurement by moving viewer method
The emittance  can also be measured in a drift space as shown below.
L1L1  
(xmax(V2))2 =
L = Distances between viewers
( beam profile monitors)

L1 L2
Viewer V1 V2 V3
Beam
(xmax(V3))2 =
L1 + L2)L1 + L2 ) 
where  = (xmax(V1))2


 - (
Emittance:
Discuss practical aspects
No ellipse no ? Phase space!
(13)
(14)
www.sliderbase.com
Notes: Emittance e measurement by moving viewer method
The emittance e can also be measured in a drift space as shown below.
s11 + 2 L1 s12 + L1 2 s22
(xmax(V2))2 =
L = Distances between viewers
( beam profile monitors)
¾½¾¾¾½¾¾¾¾½¾®
L1 L2
Viewer V1 V2 V3
Beam
(xmax(V3))2 =
s11 + 2 (L1 + L2)s12 + (L1 + L2 )2 s22
where s11 = (xmax(V1))2
e = Ö
```````````
s11s22 - (s12) 2
Emittance:
Discuss practical aspects
No ellipse no e? Phase space!
(13)
(14)
www.sliderbase.com
Emittance e measurement by moving viewer method
The emittance e can also be measured in a drift space as shown below.
s11 + 2 L1 s12 + L1 2 s22
(xmax(V2))2 =
L = Distances between viewers
( beam profile monitors)
¾½¾¾¾½¾¾¾¾½¾®
L1 L2
Viewer V1 V2 V3
Beam
(xmax(V3))2 =
s11 + 2 (L1 + L2)s12 + (L1 + L2 )2 s22
where s11 = (xmax(V1))2
e = Ö
```````````
s11s22 - (s12) 2
Emittance:
Discuss practical aspects
No ellipse no e? Phase space!
(13)
(14)
www.sliderbase.com

## Slide 25: Taylor expansion
Linear (1st order)TRANSPORT Matrix Rnm
,l
Note: Several notations are in use for 6 dim. ray vector & matrix elements.
Remarks:
Midplane symmetry of magnets
reason for many matrix element = 0
Linear approx. for “well” designed
magnets and paraxial beams
TRANSPORT code calculates 2nd order
by including Tmno elements explicitly
TRANSPORT formalism is not suitable
to calculate higher order ( >2 ).
TRANSPORT RAYTRACE
Notation
Rnm = (n|m)
(15)
www.sliderbase.com
Notes: Taylor expansion
Linear (1st order)TRANSPORT Matrix Rnm
,l
Note: Several notations are in use for 6 dim. ray vector & matrix elements.
Remarks:
Midplane symmetry of magnets
reason for many matrix element = 0
Linear approx. for “well” designed
magnets and paraxial beams
TRANSPORT code calculates 2nd order
by including Tmno elements explicitly
TRANSPORT formalism is not suitable
to calculate higher order ( >2 ).
TRANSPORT RAYTRACE
Notation
Rnm = (n|m)
(15)
www.sliderbase.com
Taylor expansion
Linear (1st order)TRANSPORT Matrix Rnm
,l
Note: Several notations are in use for 6 dim. ray vector & matrix elements.
Remarks:
Midplane symmetry of magnets
reason for many matrix element = 0
Linear approx. for “well” designed
magnets and paraxial beams
TRANSPORT code calculates 2nd order
by including Tmno elements explicitly
TRANSPORT formalism is not suitable
to calculate higher order ( >2 ).
TRANSPORT RAYTRACE
Notation
Rnm = (n|m)
(15)
www.sliderbase.com

## Slide 26: Solving the equations of Motion
Methods of solving the equation of motion:
1) Determine the TRANSPORT matrix.
2) Code RAYTRACE slices the system in small sections along the z-axis and integrates numerically the particle ray through the system.
3) Code COSY Infinity uses Differential Algebraic techniques to arbitrary orders using matrix representation for fast calculations
(16)
www.sliderbase.com
Notes: Solving the equations of Motion
Methods of solving the equation of motion:
1) Determine the TRANSPORT matrix.
2) Code RAYTRACE slices the system in small sections along the z-axis and integrates numerically the particle ray through the system.
3) Code COSY Infinity uses Differential Algebraic techniques to arbitrary orders using matrix representation for fast calculations
(16)
www.sliderbase.com
Solving the equations of Motion
Methods of solving the equation of motion:
1) Determine the TRANSPORT matrix.
2) Code RAYTRACE slices the system in small sections along the z-axis and integrates numerically the particle ray through the system.
3) Code COSY Infinity uses Differential Algebraic techniques to arbitrary orders using matrix representation for fast calculations
(16)
www.sliderbase.com

## Slide 27: Discussion of Diagnostic Elements
Some problems:
Range < 1 to > 1012 particles/s
Interference with beam, notably at low energies
Cost can be very high
Signal may not represent beam properties (e.g. blind viewer spot)
Some solutions:
Viewers, scintillators, quartz with CCD readout
Slits (movable) Faraday cups (current readout)
Harps, electronic readout, semi- transparent
Film (permanent record, dosimetry, e.g. in Proton Therapy)
Wire chambers (Spectrometer)
Faint beam 1012  103 (Cyclotrons: MSU, RCNP, iThemba)
www.sliderbase.com
Notes: Discussion of Diagnostic Elements
Some problems:
Range < 1 to > 1012 particles/s
Interference with beam, notably at low energies
Cost can be very high
Signal may not represent beam properties (e.g. blind viewer spot)
Some solutions:
Viewers, scintillators, quartz with CCD readout
Slits (movable) Faraday cups (current readout)
Harps, electronic readout, semi- transparent
Film (permanent record, dosimetry, e.g. in Proton Therapy)
Wire chambers (Spectrometer)
Faint beam 1012 ® 103 (Cyclotrons: MSU, RCNP, iThemba)
www.sliderbase.com
Discussion of Diagnostic Elements
Some problems:
Range < 1 to > 1012 particles/s
Interference with beam, notably at low energies
Cost can be very high
Signal may not represent beam properties (e.g. blind viewer spot)
Some solutions:
Viewers, scintillators, quartz with CCD readout
Slits (movable) Faraday cups (current readout)
Harps, electronic readout, semi- transparent
Film (permanent record, dosimetry, e.g. in Proton Therapy)
Wire chambers (Spectrometer)
Faint beam 1012 ® 103 (Cyclotrons: MSU, RCNP, iThemba)
www.sliderbase.com

## Slide 28: Diagnostics in focal plane of spectrometer
Typical in focal plane of
Modern Spectrometers:
Two position sensitive
Detectors:
Horizontal: X1, X2
Vertical: Y1, Y2
Fast plastic scintillators:
Particle identification
Time-of-Flight
Measurement with IUCF K600
Spectrometer illustrates from top
to bottom: focus near, down-
stream and upstream of
X1 detector, respectively
IUCF, K600 Spectrometer
www.sliderbase.com
Notes: Diagnostics in focal plane of spectrometer
Typical in focal plane of
Modern Spectrometers:
Two position sensitive
Detectors:
Horizontal: X1, X2
Vertical: Y1, Y2
Fast plastic scintillators:
Particle identification
Time-of-Flight
Measurement with IUCF K600
Spectrometer illustrates from top
to bottom: focus near, down-
stream and upstream of
X1 detector, respectively
IUCF, K600 Spectrometer
www.sliderbase.com
Diagnostics in focal plane of spectrometer
Typical in focal plane of
Modern Spectrometers:
Two position sensitive
Detectors:
Horizontal: X1, X2
Vertical: Y1, Y2
Fast plastic scintillators:
Particle identification
Time-of-Flight
Measurement with IUCF K600
Spectrometer illustrates from top
to bottom: focus near, down-
stream and upstream of
X1 detector, respectively
IUCF, K600 Spectrometer
www.sliderbase.com

## Slide 29: Higher order beam aberrations
Detector X1 X2
3 rays in focal plane
1.
2.
1.
2.
3.
Example Octupole
(S-shape in x- plane
Other Example:
Sextupole T122
C-shape in x- plot
3.
T1222
T126
www.sliderbase.com
Notes: Higher order beam aberrations
Detector X1 X2
3 rays in focal plane
1.
2.
1.
2.
3.
Example Octupole
(S-shape in x-Q plane
Other Example:
Sextupole T122
C-shape in x-Q plot
3.
T1222
T126
www.sliderbase.com
Higher order beam aberrations
Detector X1 X2
3 rays in focal plane
1.
2.
1.
2.
3.
Example Octupole
(S-shape in x-Q plane
Other Example:
Sextupole T122
C-shape in x-Q plot
3.
T1222
T126
www.sliderbase.com