## Slide 1: Chapter 5
Using Electricity in the Home
Notes: Chapter 5
Using Electricity in the Home
Chapter 5
Using Electricity in the Home

## Slide 2: Work = force (Newtons) X distance (m)
In order to do work a force must move through a distance.
Kinetic energy involves movement or use
Potential energy means that it can be used
On Earth we can convert our weight in kilograms to Newtons by multiplying by 10 i.e.. One kilogram becomes 10 N
Notes: Work = force (Newtons) X distance (m)
In order to do work a force must move through a distance.
Kinetic energy involves movement or use
Potential energy means that it can be used
On Earth we can convert our weight in kilograms to Newtons by multiplying by 10 i.e.. One kilogram becomes 10 N
Work = force (Newtons) X distance (m)
In order to do work a force must move through a distance.
Kinetic energy involves movement or use
Potential energy means that it can be used
On Earth we can convert our weight in kilograms to Newtons by multiplying by 10 i.e.. One kilogram becomes 10 N

## Slide 3: Energy = Voltage X Current X time
The units for energy are joules (J)
Power = energy / time
Power = Voltage (v) X Current (I)
Notes: Energy = Voltage X Current X time
The units for energy are joules (J)
Power = energy / time
Power = Voltage (v) X Current (I)
Energy = Voltage X Current X time
The units for energy are joules (J)
Power = energy / time
Power = Voltage (v) X Current (I)

## Slide 4: House Hold Energy Consumption
Hydro bills are established by finding out how many kilowatt hours of electricity your household has used in a given time.
1 kWh = kilowatts X time (hours)
1 kWh = 1 000 Watts X 1 hour
1 kWh = 1 000 W X 3 600 seconds
Notes: House Hold Energy Consumption
Hydro bills are established by finding out how many kilowatt hours of electricity your household has used in a given time.
1 kWh = kilowatts X time (hours)
1 kWh = 1 000 Watts X 1 hour
1 kWh = 1 000 W X 3 600 seconds
House Hold Energy Consumption
Hydro bills are established by finding out how many kilowatt hours of electricity your household has used in a given time.
1 kWh = kilowatts X time (hours)
1 kWh = 1 000 Watts X 1 hour
1 kWh = 1 000 W X 3 600 seconds

## Slide 5: Reading the Meter – always use the smallest number
Notes: Reading the Meter – always use the smallest number
Reading the Meter – always use the smallest number

## Slide 6: This reading should be 88762
Notes: This reading should be 88762
This reading should be 88762

## Slide 7: Efficiency
This is a comparison of the amount of energy obtained as compared to the amount of energy put into the system
Efficiency = energy output / energy input
To convert it to a percentage just multiply the answer by 100 %
Notes: Efficiency
This is a comparison of the amount of energy obtained as compared to the amount of energy put into the system
Efficiency = energy output / energy input
To convert it to a percentage just multiply the answer by 100 %
Efficiency
This is a comparison of the amount of energy obtained as compared to the amount of energy put into the system
Efficiency = energy output / energy input
To convert it to a percentage just multiply the answer by 100 %

## Slide 8: House Hold Wiring
The wires coming into a house include a black, a red and a white.
The black and the red wires are “hot”
The white wire is neutral – leading to a ground
The black is rated as being 120 v from the neutral
The red is rated as being 120 v from the neutral
Notes: House Hold Wiring
The wires coming into a house include a black, a red and a white.
The black and the red wires are “hot”
The white wire is neutral – leading to a ground
The black is rated as being 120 v from the neutral
The red is rated as being 120 v from the neutral
House Hold Wiring
The wires coming into a house include a black, a red and a white.
The black and the red wires are “hot”
The white wire is neutral – leading to a ground
The black is rated as being 120 v from the neutral
The red is rated as being 120 v from the neutral

## Slide 9: Electricity Entering Your House
Red = In at 120V
Black = Out at 120V
Potential difference = 240V
Notes: Electricity Entering Your House
Red = In at 120V
Black = Out at 120V
Potential difference = 240V
Electricity Entering Your House
Red = In at 120V
Black = Out at 120V
Potential difference = 240V

## Slide 10: Household Wiring is in Parallel
 | Which connecting wire, A, B, C, D, or E, will be the first to become dangerously hot if too many appliances are turned on? How can overheating be prevented, even if all the appliances in the house are turned on
Notes: Household Wiring is in Parallel
Household Wiring is in Parallel

## Slide 11: Alternating Current Frequency
In North America, the current alternates back and forth in what we call cycles per second
1 cycle/second = 1 Hertz
Electrical frequency in North America = 60 Hz
Notes: Alternating Current Frequency
In North America, the current alternates back and forth in what we call cycles per second
1 cycle/second = 1 Hertz
Electrical frequency in North America = 60 Hz
Alternating Current Frequency
In North America, the current alternates back and forth in what we call cycles per second
1 cycle/second = 1 Hertz
Electrical frequency in North America = 60 Hz

## Slide 12: The Service Panel
Since the service panel has black, red, and white wires, the total voltage is 120 + 120 = 240 volts.
The service panel usually contains circuit breakers. The breakers have either a red or a black wire attached to them.
The service panel provides electricity for the branch circuits.
Notes: The Service Panel
Since the service panel has black, red, and white wires, the total voltage is 120 + 120 = 240 volts.
The service panel usually contains circuit breakers. The breakers have either a red or a black wire attached to them.
The service panel provides electricity for the branch circuits.
The Service Panel
Since the service panel has black, red, and white wires, the total voltage is 120 + 120 = 240 volts.
The service panel usually contains circuit breakers. The breakers have either a red or a black wire attached to them.
The service panel provides electricity for the branch circuits.

## Slide 13
Usually 15 amp breaker
30 amps or greater
Notes: Usually 15 amp breaker
30 amps or greater
Usually 15 amp breaker
30 amps or greater

## Slide 14: Powerful Devices
Notes: Powerful Devices
Powerful Devices

## Slide 15: The Neutral Wire (White)
The neutral wire is the ground
Grounds protect us from electrocution
Service Panel has a ground wire
3 prong plug – the circular, bottom hole leads to the ground buried outside.
Notes: The Neutral Wire (White)
The neutral wire is the ground
Grounds protect us from electrocution
Service Panel has a ground wire
3 prong plug – the circular, bottom hole leads to the ground buried outside.
The Neutral Wire (White)
The neutral wire is the ground
Grounds protect us from electrocution
Service Panel has a ground wire
3 prong plug – the circular, bottom hole leads to the ground buried outside.

## Slide 16: The Neutral Wire (White)
The neutral wire is _____________
Grounds protect us from __________
Service Panel has a ______________
3 prong plug – the circular, bottom hole _________________________________.
Notes: The Neutral Wire (White)
The neutral wire is _____________
Grounds protect us from __________
Service Panel has a ______________
3 prong plug – the circular, bottom hole _________________________________.
The Neutral Wire (White)
The neutral wire is _____________
Grounds protect us from __________
Service Panel has a ______________
3 prong plug – the circular, bottom hole _________________________________.

## Slide 17: Three Prong Plug
Notes: Three Prong Plug
Three Prong Plug

## Slide 19: Circuit Breakers
Circuit breakers open the circuit when a current in a house wire exceeds the rated current for that circuit.
The circuit breaker protects people from being electrocuted to death and protects us from burning down the house.
Circuit overloads cause the generation of heat.
Notes: Circuit Breakers
Circuit breakers open the circuit when a current in a house wire exceeds the rated current for that circuit.
The circuit breaker protects people from being electrocuted to death and protects us from burning down the house.
Circuit overloads cause the generation of heat.
Circuit Breakers
Circuit breakers open the circuit when a current in a house wire exceeds the rated current for that circuit.
The circuit breaker protects people from being electrocuted to death and protects us from burning down the house.
Circuit overloads cause the generation of heat.

## Slide 21: Circuit breakers - Details
Ordinary breakers are rated as 15 amps.
There are bigger breakers provided for such circuits that require 240 volts – e.g.. Dryers and water heaters.
Instead of circuit breakers some electrical devices have fuses. Often electric stoves have fuses.
Notes: Circuit breakers - Details
Ordinary breakers are rated as 15 amps.
There are bigger breakers provided for such circuits that require 240 volts – e.g.. Dryers and water heaters.
Instead of circuit breakers some electrical devices have fuses. Often electric stoves have fuses.
Circuit breakers - Details
Ordinary breakers are rated as 15 amps.
There are bigger breakers provided for such circuits that require 240 volts – e.g.. Dryers and water heaters.
Instead of circuit breakers some electrical devices have fuses. Often electric stoves have fuses.

## Slide 22: Fuses are Older than Circuit of Breakers
When ribbon carries too much current, it melts, interrupting the current.
Notes: Fuses are Older than Circuit of Breakers
Fuses are Older than Circuit of Breakers

## Slide 23: GFCI – Ground Fault Circuit Interrupter
Detects current differences in the neutral and hot wire
Should be same
If not, the internal breaker goes immediately
Can reset
Use near water sources – where safety is concern
Bathroom, outdoor outlets
Notes: GFCI – Ground Fault Circuit Interrupter
Detects current differences in the neutral and hot wire
Should be same
If not, the internal breaker goes immediately
Can reset
Use near water sources – where safety is concern
Bathroom, outdoor outlets
GFCI – Ground Fault Circuit Interrupter
Detects current differences in the neutral and hot wire
Should be same
If not, the internal breaker goes immediately
Can reset
Use near water sources – where safety is concern
Bathroom, outdoor outlets

## Slide 24: House Hold Wiring
House hold circuits are 120 volts and are alternating current. Appliances are usually connected in parallel.
The circuits are polarized. That is, the black wire is connected in a certain way and the neutral wire is connected in a certain way.
Polarized plugs reduce the risk of an electrical shock by forcing electricity to flow in one general direction
Notes: House Hold Wiring
House hold circuits are 120 volts and are alternating current. Appliances are usually connected in parallel.
The circuits are polarized. That is, the black wire is connected in a certain way and the neutral wire is connected in a certain way.
Polarized plugs reduce the risk of an electrical shock by forcing electricity to flow in one general direction
House Hold Wiring
House hold circuits are 120 volts and are alternating current. Appliances are usually connected in parallel.
The circuits are polarized. That is, the black wire is connected in a certain way and the neutral wire is connected in a certain way.
Polarized plugs reduce the risk of an electrical shock by forcing electricity to flow in one general direction

## Slide 25
Types of Plugs Used in the Home
Drier Plug or Stove Plug
(Ground)
Lamp Plug or Hair Dryer
(Polarized)
Notes: Types of Plugs Used in the Home
Drier Plug or Stove Plug
(Ground)
Lamp Plug or Hair Dryer
(Polarized)
Types of Plugs Used in the Home
Drier Plug or Stove Plug
(Ground)
Lamp Plug or Hair Dryer
(Polarized)

## Slide 26: Three Prong Plug
Notes: Three Prong Plug
Three Prong Plug

## Slide 27: Three pronged plug
The round prong is the ground
The longer hole is connected to the white wire (neutral). We need this wire to complete the circuit.
The shorter hole is connected to the black wire.(hot – 120 Volts)
The grounded plug is safer than a two pronged plug.
Notes: Three pronged plug
The round prong is the ground
The longer hole is connected to the white wire (neutral). We need this wire to complete the circuit.
The shorter hole is connected to the black wire.(hot – 120 Volts)
The grounded plug is safer than a two pronged plug.
Three pronged plug
The round prong is the ground
The longer hole is connected to the white wire (neutral). We need this wire to complete the circuit.
The shorter hole is connected to the black wire.(hot – 120 Volts)
The grounded plug is safer than a two pronged plug.

## Slide 28: Grounding the Current
The service panel is connected to a long metal stake that buried outside the house.
If a person is electrocuted most of the current will go to ground.
In much older houses the wiring is grounded on the copper water pipes.
Notes: Grounding the Current
The service panel is connected to a long metal stake that buried outside the house.
If a person is electrocuted most of the current will go to ground.
In much older houses the wiring is grounded on the copper water pipes.
Grounding the Current
The service panel is connected to a long metal stake that buried outside the house.
If a person is electrocuted most of the current will go to ground.
In much older houses the wiring is grounded on the copper water pipes.

## Slide 29
Ground Wire
Notes: Ground Wire
Ground Wire

## Slide 30
Improperly Grounded Appliance with Short
One milliampere: tingling sensation Ten milliamperes: nerves and muscles overloaded 200 milliamperes: potentially fatal; heart fibrillation 500 -1000 milliamperes: not necessarily fatal; heart will restart -- One ampere or more: burn alive
Notes: Improperly Grounded Appliance with Short
One milliampere: tingling sensation Ten milliamperes: nerves and muscles overloaded 200 milliamperes: potentially fatal; heart fibrillation 500 -1000 milliamperes: not necessarily fatal; heart will restart -- One ampere or more: burn alive
Improperly Grounded Appliance with Short
One milliampere: tingling sensation Ten milliamperes: nerves and muscles overloaded 200 milliamperes: potentially fatal; heart fibrillation 500 -1000 milliamperes: not necessarily fatal; heart will restart -- One ampere or more: burn alive

## Slide 32
Grounded Appliance
Notes: Grounded Appliance
Grounded Appliance

## Slide 33: Ground Plugs Prevent You from becoming the Shortest, Easiest Path to the Ground!! 
Notes: Ground Plugs Prevent You from becoming the Shortest, Easiest Path to the Ground!! 
Ground Plugs Prevent You from becoming the Shortest, Easiest Path to the Ground!! 

## Slide 34: Avoid! Or.. Thou Shalt Not! …
Frayed electrical wires
Octopus outlets
Water and electrical wires
Plug receptacles to protect small children
Over loading electrical circuits
Notes: Avoid! Or.. Thou Shalt Not! …
Frayed electrical wires
Octopus outlets
Water and electrical wires
Plug receptacles to protect small children
Over loading electrical circuits
Avoid! Or.. Thou Shalt Not! …
Frayed electrical wires
Octopus outlets
Water and electrical wires
Plug receptacles to protect small children
Over loading electrical circuits