## Slide 1: Class Opener: How are Satellites classified? What country launched the first satellite?
Notes: Class Opener: How are Satellites classified? What country launched the first satellite?

## Slide 2: Satellite Orbits and Uses
Grade 11 Physics
NIS, Taldykorgan
Mr. Marty
Notes: Satellite Orbits and Uses
Grade 11 Physics
NIS, Taldykorgan
Mr. Marty

## Slide 3: Objectives:
describe motion of spacecraft
  Derive the expression for escape velocity.
  Calculate energy changes in the gravitational field for spacecraft leaving the Earth and the solar system
show an understanding of geostationary orbits and their application
Notes: Objectives:
describe motion of spacecraft
Derive the expression for escape velocity.
Calculate energy changes in the gravitational field for spacecraft leaving the Earth and the solar system
show an understanding of geostationary orbits and their application

## Slide 4: Why do you need to know about Satellites
Russia's Sputnik 1, the world's first man-made satellite was launched from Baykonur Cosmodrome!
Baykonur is used for many Satellite rocket launches!
International Launch Services is an unparalleled success in the space industry setting the standard for Russian-American space cooperation. http://www.ilslaunch.com/about-us/ils-legacy
Baykonur has many jobs for engineers and scientists!
Notes: Why do you need to know about Satellites
Russia's Sputnik 1, the world's first man-made satellite was launched from Baykonur Cosmodrome!
Baykonur is used for many Satellite rocket launches!
International Launch Services is an unparalleled success in the space industry setting the standard for Russian-American space cooperation. http://www.ilslaunch.com/about-us/ils-legacy
Baykonur has many jobs for engineers and scientists!

## Slide 5: PLACING SATELLITES IN ORBIT
DELTA II
TAURUS
TITAN IV
Notes: PLACING SATELLITES IN ORBIT
DELTA II
TAURUS
TITAN IV
PLACING SATELLITES IN ORBIT
DELTA II
TAURUS
TITAN IV
PLACING SATELLITES IN ORBIT
DELTA II
TAURUS
TITAN IV
PLACING SATELLITES IN ORBIT
DELTA II
TAURUS
TITAN IV
PLACING SATELLITES IN ORBIT
DELTA II
TAURUS
TITAN IV
PLACING SATELLITES IN ORBIT
DELTA II
TAURUS
TITAN IV
PLACING SATELLITES IN ORBIT
DELTA II
TAURUS
TITAN IV
PLACING SATELLITES IN ORBIT
DELTA II
TAURUS
TITAN IV
PLACING SATELLITES IN ORBIT
DELTA II
TAURUS
TITAN IV

## Slide 6: TYPES OF ORBITS
LEO Low Earth Orbit, Polar
MEO Medium Earth Orbit, polar and elliptical
HEO High Earth Orbit, geostationary
GEO Geosynchronous Orbit
Notes: TYPES OF ORBITS
LEO Low Earth Orbit, Polar
MEO Medium Earth Orbit, polar and elliptical
HEO High Earth Orbit, geostationary
GEO Geosynchronous Orbit
TYPES OF ORBITS
LEO Low Earth Orbit, Polar
MEO Medium Earth Orbit, polar and elliptical
HEO High Earth Orbit, geostationary
GEO Geosynchronous Orbit
TYPES OF ORBITS
LEO Low Earth Orbit, Polar
MEO Medium Earth Orbit, polar and elliptical
HEO High Earth Orbit, geostationary
GEO Geosynchronous Orbit
TYPES OF ORBITS
LEO Low Earth Orbit, Polar
MEO Medium Earth Orbit, polar and elliptical
HEO High Earth Orbit, geostationary
GEO Geosynchronous Orbit
TYPES OF ORBITS
LEO Low Earth Orbit, Polar
MEO Medium Earth Orbit, polar and elliptical
HEO High Earth Orbit, geostationary
GEO Geosynchronous Orbit
TYPES OF ORBITS
LEO Low Earth Orbit, Polar
MEO Medium Earth Orbit, polar and elliptical
HEO High Earth Orbit, geostationary
GEO Geosynchronous Orbit
TYPES OF ORBITS
LEO Low Earth Orbit, Polar
MEO Medium Earth Orbit, polar and elliptical
HEO High Earth Orbit, geostationary
GEO Geosynchronous Orbit
TYPES OF ORBITS
LEO Low Earth Orbit, Polar
MEO Medium Earth Orbit, polar and elliptical
HEO High Earth Orbit, geostationary
GEO Geosynchronous Orbit
TYPES OF ORBITS
LEO Low Earth Orbit, Polar
MEO Medium Earth Orbit, polar and elliptical
HEO High Earth Orbit, geostationary
GEO Geosynchronous Orbit

## Slide 7: Low-Earth-Orbit (LEO = Polar)
Altitude (600 to 1600 km)
Revolution time: 90 min - 3 hours.
Advantages:
  Reduces transmission delay
  Eliminates need for bulky receiving equipment.
Disadvantages:
  Smaller coverage area.
  Shorter life span (5-8 yrs.) than GEOs (10 yrs).
Subdivisions: Little, Big, and Mega (Super) LEOs.
Notes: Low-Earth-Orbit (LEO = Polar)
Altitude (600 to 1600 km)
Revolution time: 90 min - 3 hours.
Advantages:
Reduces transmission delay
Eliminates need for bulky receiving equipment.
Disadvantages:
Smaller coverage area.
Shorter life span (5-8 yrs.) than GEOs (10 yrs).
Subdivisions: Little, Big, and Mega (Super) LEOs.

## Slide 8: Hubble Telescope
Classification: LEO
Orbit: 375 miles, 600 km.
Revolution time: 100 min.
Speed: 7600 m/s
Concerns: Orbit decay from gravity and solar output. During “solar maximum”, the densities at all altitudes are enhanced, and the drag effects on satellites are much larger than during times of solar minimum.
Notes: Hubble Telescope
Classification: LEO
Orbit: 375 miles, 600 km.
Revolution time: 100 min.
Speed: 7600 m/s
Concerns: Orbit decay from gravity and solar output. During “solar maximum”, the densities at all altitudes are enhanced, and the drag effects on satellites are much larger than during times of solar minimum.

## Slide 9: Geosynchronous-Earth-Orbit (GEO)
Orbit is synchronous with the earths rotation.
From the ground the satellite appears fixed.
Altitude is about 36,000 km.
Coverage to 40% of planet per satellite.
Notes: Geosynchronous-Earth-Orbit (GEO)
Orbit is synchronous with the earths rotation.
From the ground the satellite appears fixed.
Altitude is about 36,000 km.
Coverage to 40% of planet per satellite.
Geosynchronous-Earth-Orbit (GEO)
Orbit is synchronous with the earths rotation.
From the ground the satellite appears fixed.
Altitude is about 36,000 km.
Coverage to 40% of planet per satellite.

## Slide 10: Basics of GEOs
Geostationary satellites are commonly used for communications and weather-observation.
The typical service life expectancy of a geostationary satellite is 10-15 years.
Because geostationary satellites circle the earth at the equator, they are not able to provide coverage at the Northernmost and Southernmost latitudes.
Notes: Basics of GEOs
Geostationary satellites are commonly used for communications and weather-observation.
The typical service life expectancy of a geostationary satellite is 10-15 years.
Because geostationary satellites circle the earth at the equator, they are not able to provide coverage at the Northernmost and Southernmost latitudes.
Basics of GEOs
Geostationary satellites are commonly used for communications and weather-observation.
The typical service life expectancy of a geostationary satellite is 10-15 years.
Because geostationary satellites circle the earth at the equator, they are not able to provide coverage at the Northernmost and Southernmost latitudes.

## Slide 11: Information on Geostationary Satellites
For a satellite to be in a particular orbit, a particular velocity is required or a given height above Earth ‘r0+h’.
Telecommunications satellites remain above one given point on the Earth’s surface, so are called geostationary
  broadcast television, forecast the weather.
Spy Satellites move in a polar orbit so that they can perform sweeps of the surface.
  spy on enemy forces
Notes: Information on Geostationary Satellites
For a satellite to be in a particular orbit, a particular velocity is required or a given height above Earth ‘r0+h’.
Telecommunications satellites remain above one given point on the Earth’s surface, so are called geostationary
broadcast television, forecast the weather.
Spy Satellites move in a polar orbit so that they can perform sweeps of the surface.
spy on enemy forces

## Slide 12: Summary of SATELLITE ORBITS
Located along the equatorial plane.
About 36000 km above the earth
Has Geo-synchronous orbit
Period of 1436 minutes
Good coverage from remote areas
Has wide field of view ~ 50 degrees
Has low resolution
Provides continuous data ~ 15-30 min.
Not very suitable for vertical soundings
Near polar orbiting
800 to 900 km above the earth
Has Sun-synchronous orbit
Period of 101 minutes
Excellent coverage at the poles
Has relatively narrow field of view
Has high resolution
Passes vary with latitude
Very suitable for vertical soundings
GEO = Geosynchronous
LEO = Polar
Notes: Located along the equatorial plane.
About 36000 km above the earth
Has Geo-synchronous orbit
Period of 1436 minutes
Good coverage from remote areas
Has wide field of view ~ 50 degrees
Has low resolution
Provides continuous data ~ 15-30 min.
Not very suitable for vertical soundings
Near polar orbiting
800 to 900 km above the earth
Has Sun-synchronous orbit
Period of 101 minutes
Excellent coverage at the poles
Has relatively narrow field of view
Has high resolution
Passes vary with latitude
Very suitable for vertical soundings
GEO = Geosynchronous
LEO = Polar
Summary of SATELLITE ORBITS
12

## Slide 13: Some Satellites in Orbit
Notes: Some Satellites in Orbit
13

## Slide 14: Geostationary Orbit Communications satellites orbit
These satellites are 36000 km above the surface and have R= 42,000km.
These satellites are positioned to orbit at rate of earths rotation and are always above the same part of the earth.
Used for TV broadcasts and mobile phones
Notes: Geostationary Orbit Communications satellites orbit
These satellites are 36000 km above the surface and have R= 42,000km.
These satellites are positioned to orbit at rate of earths rotation and are always above the same part of the earth.
Used for TV broadcasts and mobile phones

## Slide 15: GOES and POES
Geostationary Operational Environmental Satellite geo-synchronous orbit 35,800 km above the earth
Polar-orbiting Operational Environmental Satellite sun-synchronous orbit 850 km above the earth
Notes: GOES and POES
Geostationary Operational Environmental Satellite geo-synchronous orbit 35,800 km above the earth
Polar-orbiting Operational Environmental Satellite sun-synchronous orbit 850 km above the earth

## Slide 16: The GOES Spacecraft
GOES-8 Spacecraft
GOES I-M DataBook
Notes: The GOES Spacecraft
GOES-8 Spacecraft
GOES I-M DataBook

## Slide 17
GOES I-M DataBook
GOES
Notes: GOES I-M DataBook
GOES

## Slide 18: GOES Imager Products
Heavy Rainfall
High density winds
Fog/low cloud
In-flight Icing
Volcanic ash detection
Fire detection
Notes: GOES Imager Products
Heavy Rainfall
High density winds
Fog/low cloud
In-flight Icing
Volcanic ash detection
Fire detection

## Slide 19: Geostationary Satellites for Weather
http://www.ssec.wisc.edu/data/geo/
http://www.rap.ucar.edu/weather/satellite/
http://www.ssec.wisc.edu/data/volcano.html
Notes: Geostationary Satellites for Weather
http://www.ssec.wisc.edu/data/geo/
http://www.rap.ucar.edu/weather/satellite/
http://www.ssec.wisc.edu/data/volcano.html

## Slide 20
Geostationary
Notes: Geostationary

## Slide 21: 24/27 Satellites Used GPS Global Positioning System
GPS Receiver Used in Search and Rescue Missions
GPS satellites orbit Earth in 12 hours
Notes: 24/27 Satellites Used GPS Global Positioning System
GPS Receiver Used in Search and Rescue Missions
GPS satellites orbit Earth in 12 hours
24/27 Satellites Used GPS Global Positioning System
GPS Receiver Used in Search and Rescue Missions
GPS satellites orbit Earth in 12 hours
24/27 Satellites Used GPS Global Positioning System
GPS Receiver Used in Search and Rescue Missions
GPS satellites orbit Earth in 12 hours
24/27 Satellites Used GPS Global Positioning System
GPS Receiver Used in Search and Rescue Missions
GPS satellites orbit Earth in 12 hours
24/27 Satellites Used GPS Global Positioning System
GPS Receiver Used in Search and Rescue Missions
GPS satellites orbit Earth in 12 hours
24/27 Satellites Used GPS Global Positioning System
GPS Receiver Used in Search and Rescue Missions
GPS satellites orbit Earth in 12 hours
24/27 Satellites Used GPS Global Positioning System
GPS Receiver Used in Search and Rescue Missions
GPS satellites orbit Earth in 12 hours
24/27 Satellites Used GPS Global Positioning System
GPS Receiver Used in Search and Rescue Missions
GPS satellites orbit Earth in 12 hours
24/27 Satellites Used GPS Global Positioning System
GPS Receiver Used in Search and Rescue Missions
GPS satellites orbit Earth in 12 hours

## Slide 22: Ground Tracks: Westward Regression
0
30
-30
-60
-90
-120
A
B
C
A - time zero B - after one orbit C - after two orbits
60
Notes: Ground Tracks: Westward Regression
0
30
-30
-60
-90
-120
A
B
C
A - time zero B - after one orbit C - after two orbits
60
Ground Tracks: Westward Regression
0
30
-30
-60
-90
-120
A
B
C
A - time zero B - after one orbit C - after two orbits
60
Ground Tracks: Westward Regression
0
30
-30
-60
-90
-120
A
B
C
A - time zero B - after one orbit C - after two orbits
60
Ground Tracks: Westward Regression
0
30
-30
-60
-90
-120
A
B
C
A - time zero B - after one orbit C - after two orbits
60
Ground Tracks: Westward Regression
0
30
-30
-60
-90
-120
A
B
C
A - time zero B - after one orbit C - after two orbits
60
Ground Tracks: Westward Regression
0
30
-30
-60
-90
-120
A
B
C
A - time zero B - after one orbit C - after two orbits
60
Ground Tracks: Westward Regression
0
30
-30
-60
-90
-120
A
B
C
A - time zero B - after one orbit C - after two orbits
60
Ground Tracks: Westward Regression
0
30
-30
-60
-90
-120
A
B
C
A - time zero B - after one orbit C - after two orbits
60
Ground Tracks: Westward Regression
0
30
-30
-60
-90
-120
A
B
C
A - time zero B - after one orbit C - after two orbits
60

## Slide 23: Ground tracks: Inclination to equator
60
30
0
30
60
45N
45S
Inclination = 45 degrees Eccentricity ~ 0
Notes: Ground tracks: Inclination to equator
60
30
0
30
60
45N
45S
Inclination = 45 degrees Eccentricity ~ 0
Ground tracks: Inclination to equator
60
30
0
30
60
45N
45S
Inclination = 45 degrees Eccentricity ~ 0
Ground tracks: Inclination to equator
60
30
0
30
60
45N
45S
Inclination = 45 degrees Eccentricity ~ 0
Ground tracks: Inclination to equator
60
30
0
30
60
45N
45S
Inclination = 45 degrees Eccentricity ~ 0
Ground tracks: Inclination to equator
60
30
0
30
60
45N
45S
Inclination = 45 degrees Eccentricity ~ 0
Ground tracks: Inclination to equator
60
30
0
30
60
45N
45S
Inclination = 45 degrees Eccentricity ~ 0
Ground tracks: Inclination to equator
60
30
0
30
60
45N
45S
Inclination = 45 degrees Eccentricity ~ 0
Ground tracks: Inclination to equator
60
30
0
30
60
45N
45S
Inclination = 45 degrees Eccentricity ~ 0
Ground tracks: Inclination to equator
60
30
0
30
60
45N
45S
Inclination = 45 degrees Eccentricity ~ 0

## Slide 24
Ground Track of Geostationary orbit with 450 angle to equator
Ground Track Slides Courtesy of Major David French
Notes: Ground Track of Geostationary orbit with 450 angle to equator
Ground Track Slides Courtesy of Major David French

## Slide 25: Ground Tracks: with eccentricity
Ground Track for Molnyia orbit eccentricity = .7252
Notes: Ground Tracks: with eccentricity
Ground Track for Molnyia orbit eccentricity = .7252
Ground Tracks: with eccentricity
Ground Track for Molnyia orbit eccentricity = .7252
Ground Tracks: with eccentricity
Ground Track for Molnyia orbit eccentricity = .7252
Ground Tracks: with eccentricity
Ground Track for Molnyia orbit eccentricity = .7252
Ground Tracks: with eccentricity
Ground Track for Molnyia orbit eccentricity = .7252
Ground Tracks: with eccentricity
Ground Track for Molnyia orbit eccentricity = .7252
Ground Tracks: with eccentricity
Ground Track for Molnyia orbit eccentricity = .7252
Ground Tracks: with eccentricity
Ground Track for Molnyia orbit eccentricity = .7252
Ground Tracks: with eccentricity
Ground Track for Molnyia orbit eccentricity = .7252

## Slide 26
Geosynchronous
Notes: Geosynchronous

## Slide 27
e = 0
e = 0
i = 0°
Geosynchronous
e = 0.4
w = 180°
e = 0.6
w = 90°
Notes: e = 0
e = 0
i = 0°
Geosynchronous
e = 0.4
w = 180°
e = 0.6
w = 90°

## Slide 28: METEOROLOGICAL SATELLITES
For monitoring the environment, there are three types namely the:
  Weather satellites, GEO
  Meteorological climate research, Polar orbit
  Earth Resource satellites (ERS)
  Research and Development satellites (R&D).
Notes: METEOROLOGICAL SATELLITES
For monitoring the environment, there are three types namely the:
Weather satellites, GEO
Meteorological climate research, Polar orbit
Earth Resource satellites (ERS)
Research and Development satellites (R&D).
28

## Slide 29: Orbit of a Polar-Orbiting Satellite
http://coastwatch.glerl.noaa.gov/modis/modis.cgi/modis?region=s&page=1
Notes: 29
Orbit of a Polar-Orbiting Satellite
http://coastwatch.glerl.noaa.gov/modis/modis.cgi/modis?region=s&page=1

## Slide 30
LEO orbit at a height of about 500km (this is quite low!)
They take about 90 minutes to do one complete orbit.
These satellites are used to monitor things like climate research and enemy troop movements.
Polar Orbits are also called Monitoring satellites
Notes: LEO orbit at a height of about 500km (this is quite low!)
They take about 90 minutes to do one complete orbit.
These satellites are used to monitor things like climate research and enemy troop movements.
Polar Orbits are also called Monitoring satellites

## Slide 31: POES Defense Meteorological Satellite Program (DMSP)
Sensors of interest
Special Sensor Microwave / Imager (SSM/I)
Special Sensor Microwave / Temperature (SSM/T) – Atmospheric Temperature Profiler
SSM/T2 – Atmospheric Water Vapor Profiler
http://dmsp.ngdc.noaa.gov/dmsp.html
Notes: POES Defense Meteorological Satellite Program (DMSP)
Sensors of interest
Special Sensor Microwave / Imager (SSM/I)
Special Sensor Microwave / Temperature (SSM/T) – Atmospheric Temperature Profiler
SSM/T2 – Atmospheric Water Vapor Profiler
http://dmsp.ngdc.noaa.gov/dmsp.html

## Slide 32: Conical Scanning –SSM/I
Polar Satellite Products for the Operational Forecaster – COMET CD
Notes: Conical Scanning –SSM/I
Polar Satellite Products for the Operational Forecaster – COMET CD

## Slide 33: Orbital Coverage
Introduction to POES data and products – COMET/VISIT teletraining
Satellite makes one orbit (360°) in about 100 min; i.e., it goes about 3.6°/min, or about 10° in 3 minutes.
With a knowledge of which way the satellite is moving and how fast it is moving, one can estimate viewing time at a particular point.
Notes: Orbital Coverage
Introduction to POES data and products – COMET/VISIT teletraining
Satellite makes one orbit (360°) in about 100 min; i.e., it goes about 3.6°/min, or about 10° in 3 minutes.
With a knowledge of which way the satellite is moving and how fast it is moving, one can estimate viewing time at a particular point.

## Slide 34: AMSU coverage (2200 km swath)
http://amsu.cira.colostate.edu/
Notes: AMSU coverage (2200 km swath)
http://amsu.cira.colostate.edu/

## Slide 35
SSMI coverage (1400 km swath)
Example from NOAA’s Marine Observing Systems Team Web Page
http://manati.orbit.nesdis.noaa.gov/doc/ssmiwinds.html
swath
Notes: SSMI coverage (1400 km swath)
Example from NOAA’s Marine Observing Systems Team Web Page
http://manati.orbit.nesdis.noaa.gov/doc/ssmiwinds.html
swath

## Slide 36: AVHRR Products
Sea Surface Temperature (SST)
Normalized Difference Vegetation Index (NDVI)
Atmospheric aerosols
Volcanic Ash detection
Fire detection
SST
NDVI
Aerosols
Fires
Volcanic Ash
Notes: AVHRR Products
Sea Surface Temperature (SST)
Normalized Difference Vegetation Index (NDVI)
Atmospheric aerosols
Volcanic Ash detection
Fire detection
SST
NDVI
Aerosols
Fires
Volcanic Ash

## Slide 37: AMSU/SSMI Products
Total Precipitable Water (TPW)
Cloud Liquid Water (CLW)
Rain rate
Snow and Ice cover
TPW
CLW
Rain rate
Snow cover
Ice cover
http://amsu.cira.colostate.edu/
Notes: AMSU/SSMI Products
Total Precipitable Water (TPW)
Cloud Liquid Water (CLW)
Rain rate
Snow and Ice cover
TPW
CLW
Rain rate
Snow cover
Ice cover
http://amsu.cira.colostate.edu/

## Slide 38: Space Debris
According to the U.S. Space Command (USSC), there are more than 8,000 objects larger than a softball now circling the globe.
Of these, over 2000 are satellites (working and not).
Notes: Space Debris
According to the U.S. Space Command (USSC), there are more than 8,000 objects larger than a softball now circling the globe.
Of these, over 2000 are satellites (working and not).

## Slide 39: Diagram of Kepler’s Second Law
Equal Areas in Equal times: The line joining the planet to the Sun sweeps out equal areas in equal times as the planet travels around the ellipse.
Notes: Diagram of Kepler’s Second Law
Equal Areas in Equal times: The line joining the planet to the Sun sweeps out equal areas in equal times as the planet travels around the ellipse.

## Slide 40: ORBIT CLASSIFICATIONS Eccentricity
Eccentricity = c/a
e = 0.75
e = .45
e = 0
Notes: ORBIT CLASSIFICATIONS Eccentricity
Eccentricity = c/a
ORBIT CLASSIFICATIONS Eccentricity
Eccentricity = c/a
ORBIT CLASSIFICATIONS Eccentricity
Eccentricity = c/a
ORBIT CLASSIFICATIONS Eccentricity
Eccentricity = c/a
ORBIT CLASSIFICATIONS Eccentricity
Eccentricity = c/a
ORBIT CLASSIFICATIONS Eccentricity
Eccentricity = c/a
ORBIT CLASSIFICATIONS Eccentricity
Eccentricity = c/a
ORBIT CLASSIFICATIONS Eccentricity
Eccentricity = c/a
ORBIT CLASSIFICATIONS Eccentricity
Eccentricity = c/a

## Slide 41: ORBITAL ELEMENTS Keplerian Elements: Inclination
Orbital Plane
Equatorial Plane
Inclination ( i )
Notes: ORBITAL ELEMENTS Keplerian Elements: Inclination
Orbital Plane
Equatorial Plane
Inclination ( i )
ORBITAL ELEMENTS Keplerian Elements: Inclination
Orbital Plane
Equatorial Plane
Inclination ( i )
ORBITAL ELEMENTS Keplerian Elements: Inclination
Orbital Plane
Equatorial Plane
Inclination ( i )
ORBITAL ELEMENTS Keplerian Elements: Inclination
Orbital Plane
Equatorial Plane
Inclination ( i )
ORBITAL ELEMENTS Keplerian Elements: Inclination
Orbital Plane
Equatorial Plane
Inclination ( i )
ORBITAL ELEMENTS Keplerian Elements: Inclination
Orbital Plane
Equatorial Plane
Inclination ( i )
ORBITAL ELEMENTS Keplerian Elements: Inclination
Orbital Plane
Equatorial Plane
Inclination ( i )
ORBITAL ELEMENTS Keplerian Elements: Inclination
Orbital Plane
Equatorial Plane
Inclination ( i )
ORBITAL ELEMENTS Keplerian Elements: Inclination
Orbital Plane
Equatorial Plane
Inclination ( i )

## Slide 42: PERTURBATIONS
Definition
  A disturbance in the regular motion of a satellite
Types
  Gravitational
  Atmospheric Drag
  Third Body Effects
  Solar Wind/Radiation Effects
  Electro-magnetic
Notes: PERTURBATIONS
Definition
A disturbance in the regular motion of a satellite
Types
Gravitational
Atmospheric Drag
Third Body Effects
Solar Wind/Radiation Effects
Electro-magnetic
PERTURBATIONS
Definition
A disturbance in the regular motion of a satellite
Types
Gravitational
Atmospheric Drag
Third Body Effects
Solar Wind/Radiation Effects
Electro-magnetic
PERTURBATIONS
Definition
A disturbance in the regular motion of a satellite
Types
Gravitational
Atmospheric Drag
Third Body Effects
Solar Wind/Radiation Effects
Electro-magnetic
PERTURBATIONS
Definition
A disturbance in the regular motion of a satellite
Types
Gravitational
Atmospheric Drag
Third Body Effects
Solar Wind/Radiation Effects
Electro-magnetic
PERTURBATIONS
Definition
A disturbance in the regular motion of a satellite
Types
Gravitational
Atmospheric Drag
Third Body Effects
Solar Wind/Radiation Effects
Electro-magnetic
PERTURBATIONS
Definition
A disturbance in the regular motion of a satellite
Types
Gravitational
Atmospheric Drag
Third Body Effects
Solar Wind/Radiation Effects
Electro-magnetic
PERTURBATIONS
Definition
A disturbance in the regular motion of a satellite
Types
Gravitational
Atmospheric Drag
Third Body Effects
Solar Wind/Radiation Effects
Electro-magnetic
PERTURBATIONS
Definition
A disturbance in the regular motion of a satellite
Types
Gravitational
Atmospheric Drag
Third Body Effects
Solar Wind/Radiation Effects
Electro-magnetic
PERTURBATIONS
Definition
A disturbance in the regular motion of a satellite
Types
Gravitational
Atmospheric Drag
Third Body Effects
Solar Wind/Radiation Effects
Electro-magnetic

## Slide 43: PERTURBATIONS Gravitational: Libration
Ellipticity of the Earth causes gravity wells and hills
Stable points: 75E and 105W
-- Himalayas and Rocky Mountains
Unstable points: 165E and 5W
-- Marshall Islands and Portugal
Drives the requirement for station keeping
Notes: PERTURBATIONS Gravitational: Libration
Ellipticity of the Earth causes gravity wells and hills
Stable points: 75E and 105W
-- Himalayas and Rocky Mountains
Unstable points: 165E and 5W
-- Marshall Islands and Portugal
Drives the requirement for station keeping
PERTURBATIONS Gravitational: Libration
Ellipticity of the Earth causes gravity wells and hills
Stable points: 75E and 105W
-- Himalayas and Rocky Mountains
Unstable points: 165E and 5W
-- Marshall Islands and Portugal
Drives the requirement for station keeping
PERTURBATIONS Gravitational: Libration
Ellipticity of the Earth causes gravity wells and hills
Stable points: 75E and 105W
-- Himalayas and Rocky Mountains
Unstable points: 165E and 5W
-- Marshall Islands and Portugal
Drives the requirement for station keeping
PERTURBATIONS Gravitational: Libration
Ellipticity of the Earth causes gravity wells and hills
Stable points: 75E and 105W
-- Himalayas and Rocky Mountains
Unstable points: 165E and 5W
-- Marshall Islands and Portugal
Drives the requirement for station keeping
PERTURBATIONS Gravitational: Libration
Ellipticity of the Earth causes gravity wells and hills
Stable points: 75E and 105W
-- Himalayas and Rocky Mountains
Unstable points: 165E and 5W
-- Marshall Islands and Portugal
Drives the requirement for station keeping
PERTURBATIONS Gravitational: Libration
Ellipticity of the Earth causes gravity wells and hills
Stable points: 75E and 105W
-- Himalayas and Rocky Mountains
Unstable points: 165E and 5W
-- Marshall Islands and Portugal
Drives the requirement for station keeping
PERTURBATIONS Gravitational: Libration
Ellipticity of the Earth causes gravity wells and hills
Stable points: 75E and 105W
-- Himalayas and Rocky Mountains
Unstable points: 165E and 5W
-- Marshall Islands and Portugal
Drives the requirement for station keeping
PERTURBATIONS Gravitational: Libration
Ellipticity of the Earth causes gravity wells and hills
Stable points: 75E and 105W
-- Himalayas and Rocky Mountains
Unstable points: 165E and 5W
-- Marshall Islands and Portugal
Drives the requirement for station keeping
PERTURBATIONS Gravitational: Libration
Ellipticity of the Earth causes gravity wells and hills
Stable points: 75E and 105W
-- Himalayas and Rocky Mountains
Unstable points: 165E and 5W
-- Marshall Islands and Portugal
Drives the requirement for station keeping

## Slide 44: PERTURBATIONS Electro-Magnetic
Interaction between the Earth’s magnetic field and the satellite’s electro-magnetic field results in magnetic drag
Notes: PERTURBATIONS Electro-Magnetic
Interaction between the Earth’s magnetic field and the satellite’s electro-magnetic field results in magnetic drag
PERTURBATIONS Electro-Magnetic
Interaction between the Earth’s magnetic field and the satellite’s electro-magnetic field results in magnetic drag
PERTURBATIONS Electro-Magnetic
Interaction between the Earth’s magnetic field and the satellite’s electro-magnetic field results in magnetic drag
PERTURBATIONS Electro-Magnetic
Interaction between the Earth’s magnetic field and the satellite’s electro-magnetic field results in magnetic drag
PERTURBATIONS Electro-Magnetic
Interaction between the Earth’s magnetic field and the satellite’s electro-magnetic field results in magnetic drag
PERTURBATIONS Electro-Magnetic
Interaction between the Earth’s magnetic field and the satellite’s electro-magnetic field results in magnetic drag
PERTURBATIONS Electro-Magnetic
Interaction between the Earth’s magnetic field and the satellite’s electro-magnetic field results in magnetic drag
PERTURBATIONS Electro-Magnetic
Interaction between the Earth’s magnetic field and the satellite’s electro-magnetic field results in magnetic drag
PERTURBATIONS Electro-Magnetic
Interaction between the Earth’s magnetic field and the satellite’s electro-magnetic field results in magnetic drag

## Slide 45: References:
http://coastwatch.glerl.noaa.gov/modis/modis.cgi/modis?region=s&page=1
http://www.ssec.wisc.edu/data/geo/
http://www.rap.ucar.edu/weather/satellite/
http://www.ssec.wisc.edu/data/volcano.html
Space Systems Loral, 1996 : GOES I-M DataBook
Can be found online at: http://rsd.gsfc.nasa.gov/goes/text/goes.databook.html
NOAA KLM User’s Guide http://www2.ncdc.noaa.gov/docs/klm/index.htm
NOAA/NESDIS Office of Satellite Operations: http://www.oso.noaa.gov/goes/index.htm
NOAA/NESDIS Office of Satellite Data Processing and Distribution http://www.osdpd.noaa.gov/
Notes: References:
http://coastwatch.glerl.noaa.gov/modis/modis.cgi/modis?region=s&page=1
http://www.ssec.wisc.edu/data/geo/
http://www.rap.ucar.edu/weather/satellite/
http://www.ssec.wisc.edu/data/volcano.html
Space Systems Loral, 1996 : GOES I-M DataBook
Can be found online at: http://rsd.gsfc.nasa.gov/goes/text/goes.databook.html
NOAA KLM User’s Guide http://www2.ncdc.noaa.gov/docs/klm/index.htm
NOAA/NESDIS Office of Satellite Operations: http://www.oso.noaa.gov/goes/index.htm
NOAA/NESDIS Office of Satellite Data Processing and Distribution http://www.osdpd.noaa.gov/